###### APPENDIX C

# PARAMETERIZATION OF DRAINAGE INPUT

# The MACRO model has been parameterised to calculate drainage inputs to surface water bodies for the six drainage scenarios, D1 to D6. Parameters in the model are listed in the following tables, sub-divided into sections on crop parameters, and soil and site parameters. The actual parameter names used in the model are given in parentheses.

# Crop parameters

# Some cropping parameters are considered as crop-specific and not site-specific, and are therefore given a common value for all drainage scenarios where the particular crop is grown (see Table 4.2.1-1). The remaining parameters, mostly concerning root depth and the crop development phases, are considered as site-specific and are therefore given different values for each scenario.

Table C.1. Crop-specific MACRO parameters for all drainage scenarios: perennial crops

|  | Crop/crop grouping |
| --- | --- |
| Input parameter | Grass+ Alfalfa | Citrus | Olives |
| Leaf area index (LAIC) | 5 | 5 | 3 |
| aRoot distribution | Medium | Deep | Deep |
| Crop height (m) (HCROP) | 0.2 | 3.0 | 3.0 |
| bDrought tolerance | Medium | Medium | Medium |
| Max. Interception capacity (mm) (CANCAP) | 2.0 | 2.0 | 1.0 |
| Ratio evaporation of intercepted water to transpiration (ZALP) | 1.0 | 2.0 | 2.0 |
| Radiation attenuation factor (ATTEN) | 0.6 | 0.45 | 0.3 |
| Stomatal resistance (s m-1) (RSURF) | 50 | 150 | 200 |

a % roots in top 25% of root depth (RPIN): shallow = 75%, medium = 67%, deep = 60%

b transpiration adaptability factor (BETA): low = 0.5, medium = 0.2, high = 0.1; critical tension for transpiration reduction (WATEN) is calculated from the known soil properties together with the % of available water exhausted before reduction in transpiration occurs: low = 50%, medium = 65%, high = 80%

Table C.2. Crop-specific MACRO parameters for all drainage scenarios: annual crops

|  | Crop /crop grouping |
| --- | --- |
| Input parameter | Cereals, winter | Cereals, spring | Oilseed rape, winter | Oilseed rape, spring | Sugar beets | Potatoes | Field beans | Veg., root | Veg., leafy | Veg., bulb |
| Maximum leaf area index (LAIMAX) | 6 | 4 | 5 | 4 | 5 | 4 | 4 | 3 | 3 | 3 |
| Green leaf area index at harvest (LAIHARV) | 2 | 2 | 2 | 2 | 5 | 2 | 3 | 3 | 3 | 3 |
| aRoot distribution | Deep | Deep | Deep | Deep | Medium | Shallow | Medium | Shallow | Shallow | Shallow |
| Max. Crop height (m) (HMAX) | 0.8 | 0.8 | 0.7 | 0.7 | 0.6 | 0.6 | 0.6 | 0.3 | 0.3 | 0.3 |
| bDrought tolerance | High | Medium | High | High | Medium | Low | Low | Low | Low | Low |
| Leaf development factor, growth (CFORM) | 2.0 | 2.0 | 2.0 | 1.7 | 1.7 | 1.7 | 1.7 | 1.5 | 1.5 | 1.5 |
| Leaf development factor, senescence (DFORM) | 0.2 | 0.3 | 0.2 | 0.2 | 1.0 | 0.3 | 0.3 | 1.0 | 1.0 | 1.0 |
| Leaf area index on specified dayd (LAIMIN) | 1.0 | 0.01 | 1.0 | 0.01 | 0.01 | 0.01 | e1.0/0.01 | 0.01 | 0.01 | c0.01 |
| Crop height on specified dayd (m) (ZHMIN) | 0.2 | 0.01 | 0.2 | 0.01 | 0.01 | 0.01 | e0.1/0.01 | 0.01 | 0.01 | c0.01 |
| Root depth on specified dayd (m) (ROOTINIT) | 0.2 | 0.01 | 0.2 | 0.01 | 0.01 | 0.01 | e0.1/0.01 | 0.01 | 0.01 | c0.01 |
| Max. Interception capacity (mm) (CANCAP) | 3 | 2 | 3 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |
| Ratio evaporation of intercepted water to transpiration (ZALP) | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 |
| Radiation attenuation factor (ATTEN) | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 |
| Min. stomatal resistance (s m-1) (RSMIN) | 50 | 50 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 |

a % roots in top 25% of root depth (RPIN): shallow = 75%, medium = 67%, deep = 60%

b transpiration adaptability factor (BETA): low = 0.5, medium = 0.2, high = 0.1; critical tension for transpiration reduction (WATEN) is calculated from the known soil properties together with the % of extractable micropore water exhausted before reduction in transpiration occurs: low = 50%, medium = 65%, high = 80%

c except scenario D6, 2nd bulb vegetable crop: LAIMIN = 0.5, ZHMIN = 0.1, ROOTINIT = 0.1

d ZDATEMIN (see Tables C3 to C8)

e autumn sown/spring sown

Table C.2 contd. : : Crop-specific MACRO parameters for all drainage scenarios : annual crops

|  | Crop /crop grouping |
| --- | --- |
| Input parameter | Legumes | Veg., fruiting | Maize | Vines | Pome/ stone fruit | Sunflowers | Cotton |
| Maximum leaf area index (LAIMAX) | 4 | 3 | 5 | 5 | 4 | 4 | 5 |
| Green leaf area index at harvest (LAIHARV) | 2 | 3 | 2 | 0.01 | 0.01 | 1 | 3 |
| aRoot distribution | Medium | Shallow | Medium | Deep | Deep | Deep | Medium |
| Max. Crop height (m) (HMAX) | 0.6 | 0.6 | 1.8 | 1.8 | 5.0 | 1.8 | 1.2 |
| bDrought tolerance | Low | Low | Medium | Medium | Medium | Medium | Medium |
| Leaf development factor, growth (CFORM) | 2.0 | 1.5 | 1.7 | 1.5 | 1.5 | 1.7 | 1.7 |
| Leaf development factor, senescence (DFORM) | 0.3 | 1.0 | 0.3 | 0.7 | 0.7 | 0.3 | 0.3 |
| Leaf area index on specified dayc (LAIMIN) | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 |
| Crop height on specified dayc (m) (ZHMIN) | 0.01 | 0.01 | 0.01 | 1.79 | 4.99 | 0.01 | 0.01 |
| Root depth on specified dayc (m) (ROOTINIT) | 0.01 | 0.01 | 0.01 | 0.99 | 0.79 | 0.01 | 0.01 |
| Max. Interception capacity (mm) (CANCAP) | 2 | 2 | 3 | 3 | 2 | 2 | 2 |
| Ratio evaporation of intercepted water to transpiration (ZALP) | 1.0 | 1.0 | 1.5 | 1.5 | 2.0 | 1.5 | 1.0 |
| Radiation attenuation factor (ATTEN) | 0.6 | 0.6 | 0.6 | 0.45 | 0.45 | 0.6 | 0.6 |
| Min. stomatal resistance (s m-1) (RSMIN) | 40 | 40 | 60 | 80 | 80 | 60 | 60 |

a % roots in top 25% of root depth (RPIN): shallow = 75%, medium = 67%, deep = 60%

b transpiration adaptability factor (BETA): low = 0.5, medium = 0.2, high = 0.1 ; critical tension for transpiration reduction (WATEN) is calculated from the known soil properties together with the % of extractable micropore water exhausted before reduction in transpiration occurs: low = 50%, medium = 65%, high = 80%

c ZDATEMIN (see Tables C3 to C8)

Table C.3. MACRO scenario-specific crop input parameters for Scenario D1

|  | Crop /crop grouping |
| --- | --- |
| Input variable | Grass + alfalfa | Cereals, winter | Cereals, spring | Oilseed rape, spring |
| Root depth (m) (ROOTMAX/ROOTDEPa) | 1.3 | 1.3 | 1.3 | 1.3 |
| Emergence (IDSTART) | - | 25/9 | 5/5 | 19/5 |
| Intermediate crop development (ZDATEMIN) | - | 25/3 | 6/5 | 20/5 |
| Max. leaf area development (IDMAX) | - | 23/6 | 28/6 | 4/7 |
| Harvest (IHARV) | - | 26/8 | 4/9 | 8/9 |

a for grass + alfalfa (perennial crop)

Table C.4. MACRO scenario-specific crop input parameters for Scenario D2

|  | Crop /crop grouping |
| --- | --- |
| Input variable | Grass + alfalfa | Cereals, winter | Oilseed rape, winter | Field beans |
| Root depth (m) (ROOTMAX/ROOTDEPa) | 0.6 | 0.6 | 0.6 | 0.6 |
| Emergence (IDSTART) | - | 25/10 | 15/9 | 12/11 |
| Intermediate crop development (ZDATEMIN) | - | 4/4 | 10/3 | 10/4 |
| Max. leaf area development (IDMAX) | - | 30/6 | 15/6 | 29/6 |
| Harvest (IHARV) | - | 7/8 | 15/7 | 15/9 |

a for grass + alfalfa (perennial crop)

Table C.5. MACRO scenario-specific crop input parameters for Scenario D3

|  | Crop /crop grouping |
| --- | --- |
| Input variable | Grass + alfalfa | Cereals, winter | Cereals, spring | Oilseed rape, winter | Oilseed rape, spring | Sugar beets | Potatoes | Field beans | Veg., root | Veg.,a leafy | Veg., bulb | Legumes | Maize | Pome/stone fruit |
| Root depth (m) (ROOTMAX/ROOTDEPb) | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.4 | 0.6 | 0.4 | 0.4 | 0.4 | 0.6 | 0.6 | 0.8 |
| Emergence (IDSTART) | - | 21/11 | 1/4 | 2/9 | 10/4 | 25/4 | 10/5 | 30/4 | 25/4 | 25/4 5/8 | 25/4 | 15/4 | 5/5 | 15/4 |
| Intermediate crop development (ZDATEMIN) | - | 16/4 | 2/4 | 21/2 | 11/4 | 26/4 | 11/5 | 1/5 | 26/4 | 26/4 6/8 | 26/4 | 16/4 | 6/5 | 16/4 |
| Max. leaf area development (IDMAX) | - | 24/7 | 5/6 | 25/5 | 15/6 | 25/7 | 20/7 | 15/7 | 30/6 | 5/6 10/9 | 30/6 | 15/6 | 10/8 | 1/7 |
| Harvest (IHARV) | - | 15/8 | 20/8 | 20/7 | 25/8 | 18/10 | 15/9 | 10/9 | 15/8 | 20/7 20/10 | 1/9 | 10/8 | 20/9 | 30/10 |

a 2 crops per season

b for grass + alfalfa (perennial crop)

Table C.6. MACRO scenario-specific crop input parameters for Scenario D4

|  | Crop /crop grouping |
| --- | --- |
| Input variable | Grass + alfalfa | Cereals, winter | Cereals, spring | Oilseed rape, winter | Oilseed rape, spring | Sugar beets | Potatoes | Field beans | Veg., leafy | Veg., bulb | Legumes | Maize | Pome/stone fruit |
| Root depth (m) (ROOTMAX/ROOTDEPa) | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 0.8 | 0.6 | 0.8 | 0.8 | 0.4 | 0.8 | 1.0 | 1.0 |
| Emergence (IDSTART) | - | 22/9 | 26/4 | 3/9 | 1/5 | 4/5 | 22/5 | 15/4 | 10/5 | 23/4 | 23/4 | 10/5 | 20/4 |
| Intermediate crop development (ZDATEMIN) | - | 18/3 | 27/4 | 1/3 | 2/5 | 5/5 | 23/5 | 16/4 | 11/5 | 24/4 | 24/4 | 11/5 | 21/4 |
| Max. leaf area development (IDMAX) | - | 21/6 | 19/6 | 5/6 | 17/6 | 28/7 | 21/8 | 10/7 | 20/7 | 10/7 | 20/6 | 18/8 | 5/7 |
| Harvest (IHARV) | - | 21/8 | 26/8 | 9/8 | 31/8 | 25/10 | 23/9 | 25/8 | 26/9 | 13/9 | 10/8 | 12/9 | 30/10 |

a for grass + alfalfa (perennial crop)

Table C.7. MACRO scenario-specific crop input parameters for Scenario D5

|  | Crop /crop grouping |
| --- | --- |
| Input variable | Grass + alfalfa | Cereals, winter | Cereals, spring | Oilseed rape, winter | Oilseed rape, spring | Legumes | Sunflowers | Maize | Pome/stone fruit |
| Root depth (m) (ROOTMAX/ROOTDEPa) | 0.9 | 0.9 | 0.7 | 0.9 | 0.7 | 0.7 | 0.9 | 0.7 | 0.9 |
| Emergence (IDSTART) | - | 10/11 | 15/3 | 20/9 | 15/3 | 15/3 | 1/5 | 10/5 | 1/4 |
| Intermediate crop development (ZDATEMIN) | - | 15/3 | 16/3 | 1/3 | 16/3 | 16/3 | 2/5 | 11/5 | 2/4 |
| Max. leaf area development (IDMAX) | - | 15/5 | 15/5 | 10/5 | 25/5 | 30/5 | 10/7 | 15/7 | 31/5 |
| Harvest (IHARV) | - | 15/7 | 20/7 | 5/7 | 30/7 | 15/7 | 31/8 | 15/9 | 10/10 |

a for grass + alfalfa (perennial crop)

Table C.8. MACRO scenario-specific crop input parameters for Scenario D6

|  | Crop /crop grouping |
| --- | --- |
| Input variable | Citrus | Olives | Maize | Cereals, winter | Potatoes | Field beansa | Veg., root | Veg., leafy | Veg.,b bulb | Legumes | Veg., fruiting | Vines | Cotton |
| Root depth (m) (ROOTMAX/ROOTDEPc) | 1.0 | 1.0 | 0.8 | 0.8 | 0.5 | 0.6 | 0.4 | 0.6 | 0.4 | 0.5 | 0.6 | 1.0 | 0.8 |
| Emergence (IDSTART) | - | - | 20/4 | 30/11 | 10/4 5/8 | 1/4 8/7 | 25/2 | 15/8 | 10/5 20/10 | 20/4 | 10/4 | 1/2 | 20/4 |
| Intermediate crop development (ZDATEMIN) | - | - | 21/4 | 16/2 | 11/4 6/8 | 2/4 9/7 | 26/2 | 16/8 | 11/5 30/1 | 21/4 | 11/4 | 2/2 | 21/4 |
| Max. leaf area development (IDMAX) | - | - | 15/6 | 30/3 | 30/5 30/9 | 1/5 8/8 | 15/4 | 30/9 | 30.6 10/3 | 20/5 | 30/5 | 1/5 | 10/6 |
| Harvest (IHARV) | - | - | 15/9 | 30/6 | 15/7 25/11 | 15/6 30/9 | 13/5 | 30/11 | 31/7 10/4 | 25/6 | 10/8 | 10/11 | 15/9 |

a 2 crops per season

b 3 crops every 2 years

c for citrus & olive (perennial crops)

# Soil and site parameters

As with crop parameters, some soil and site parameters in MACRO have been set to the same value for all scenarios (e.g. dispersion length), while others are specific to each scenario (e.g. water retention curve parameters). In the scenario-specific parameter tables, each MACRO parameter is classified into one of four groups depending on how the value was obtained (known or based on measured data, calibrated against field data, default or assumed value, estimated from pedo-transfer functions). MACRO parameter names are given in parentheses.

## Table C.9 MACRO soil parameters assumed constant for all scenarios

| Parameter | Value |
| --- | --- |
| Dispersivity (cm) (DV) | 5 |
| Mixing depth (mm) (ZMIX) | 0.1 * |
| Slope of shrinkage characteristic (ZP) | 0 |
| Geometry factor (ZA) | 1 |
| Fraction of sorption sites in macropores (FRACMAC) | 0.02 |
| Initial soil temperature (oC) (TEMPINI) | 10 |
| Initial pesticide concentration (mg m-3) (SOLINIT) | 0 |
| Pesticide concentration at bottom boundary (mg m-3) (CONCIN) | 0 |
| Critical air content for transpiration reduction (m3 m-3) (CRITAIR) | 0.05 |
| Excluded pore volume (m3 m-3) (AEXC) | 0 |

* except for soil incorporation, where ZMIX = 0.

## Table C.10. MACRO site parameters assumed constant for all scenarios

| Parameter | Value |
| --- | --- |
| Pesticide concentration in rainfall (mg m-3) (CONC) | 0 |
| Rainfall correction factor (RAINCO) | 1 |
| Snowfall correction factor (SNOWCO) | 1 |
| Rainfall intensity (mm h-1) (RINTEN) | 2 |
| Snowmelt factor (mm oC d-1) (SNOWMF) | 4.5 |
| Albedo (ALBEDO) | 0.25 |

Table C.11. Scenario-specific soil and site parameters for D1

| Horizon designation (FAO, 1990) | Ap | Bg1 | Bg2 | BCg |
| --- | --- | --- | --- | --- |
| Depth (cm) | 0-30 | 30-60 | 60-100 | 100-175 |
| BASIC PROPERTIES |  |  |  |  |
| Sand (%) | 7 | 3 | 2 | 3 |
| Silt (%) | 46 | 41 | 37 | 31 |
| Clay (%) | 47 | 56 | 61 | 66 |
| Texture (FAO, 1990; USDA, 1999) | Silty clay | silty clay | clay | Clay |
| Organic carbon (%) | 2.0 | 0.8 | 0.3 | 0.2 |
| Bulk density (g/cm3) (GAMMA) | 1.35 a | 1.42 a | 1.42 a | 1.42 c |
| pH | 7.2 | 7.4 | 7.4 | 7.6 |
| Soil structure (FAO, 1990) | Moderate medium angular blocky | moderate fine angular blocky | strong medium angular blocky | Strong coarse angular blocky |
| HYDRAULIC PROPERTIES |  |  |  |  |
| Saturated water content (%) (TPORV) | 47 a | 46 a | 47 a | 47 b |
| Wilting point (%) (WILT) | 26 a | 29 a | 31 a | 33 b |
| Residual water content (%) (RESID) | 0 a | 0 a | 0 a | 0 c |
| Water content at macro/micropore boundary (%) (XMPOR) | 40 a | 42 a | 45 a | 45 b |
| Water tension at macro/micropore boundary (cm) (CTEN) | 10 c | 10 c | 10 c | 10 c |
| Pore-size distribution index (ZLAMB) | 0.07 a | 0.05 a | 0.05 a | 0.05 b |
| Tortuosity factor micropores (ZM) | 0.5 c | 0.5 c | 0.5 c | 0.5 c |
| Tortuosity factor macropores (ZN) | 2 b | 2 b | 2 b | 2 b |
| Effective diffusion pathlength (mm) (ASCALE) | 150 b | 100 b | 300 b | 300 b |
| Saturated hydraulic conductivity (mm/hr) (KSATMIN) | 200 a | 50 a | 30 a | 20 b |
| Conductivity at macro/micropore boundary (mm/hr) (KSM) | 0.1 a | 0.3 b | 0.2 b | 0.1 b |
| FIELD DRAINAGE |  |  |  |  |
| Drain depth (m) (DRAINDEP) | 1.0 a |
| Drain spacing (m) (SPACE) | 13.5 a |
| Transmission coefficient at bottom boundary (h-1) (BGRAD) | 2.0 x 10-6 b |

a derived from measured values or known.

b calibrated.

c default or assumed value.

Table C.12. Scenario-specific soil and site parameters for D2

| Horizon designation (FAO, 1990) | Ap | Bg1 | Bg2 | Bgk | C |
| --- | --- | --- | --- | --- | --- |
| Depth (cm) | 0-20 | 20-35 | 35-65 | 65-90 | 90-150 |
| BASIC PROPERTIES |  |  |  |  |  |
| Sand (%) | 7 | 6 | 3 | 2 | 1 |
| Silt (%) | 39 | 39 | 37 | 36 | 37 |
| Clay (%) | 54 | 56 | 60 | 62 | 62 |
| Texture (FAO, 1990; USDA, 1999) | clay | clay | clay | clay | Clay |
| Organic carbon (%) | 3.3 | 0.8 | 0.7 | 0.6 | 0.6 |
| Bulk density (g/cm3) (GAMMA) | 1.20 a | 1.34 a | 1.34 a | 1.43 a | 1.43 c |
| PH | 7.0 | 7.5 | 8.0 | 8.5 | 8.5 |
| Soil structure (FAO, 1990) | moderate medium angular blocky | Strong medium angular blocky | weak very coarse prismatic | massive | Massive |
| HYDRAULIC PROPERTIES |  |  |  |  |  |
| Saturated water content (%) (TPORV) | 52 a | 48 a | 48 a | 44 a | 44 c |
| Wilting point (%) (WILT) | 25 a | 25 a | 25 a | 25 a | 25c |
| Residual water content (%) (RESID) | 0 a | 0 a | 0 a | 0 a | 0 c |
| Water content at macro/micropore boundary (%) (XMPOR) | 48 a | 47 a | 47 a | 43 a | 43 c |
| Water tension at macro/micropore boundary (cm) (CTEN) | 10 c | 10 c | 10 c | 10 c | 10 c |
| Pore-size distribution index (ZLAMB) | 0.077 a | 0.061 a | 0.048 a | 0.054 a | 0.062 d |
| Tortuosity factor micropores (ZM) | 0.5 c | 0.5 c | 0.5 c | 0.5 c | 0.5 c |
| Tortuosity factor macropores (ZN) | 2 b | 2 b | 2 b | 2 b | 2 b |
| Effective diffusion pathlength (mm) (ASCALE) | 50 b | 150 b | 150 b | 150 b | 150 b |
| Saturated hydraulic conductivity (mm/hr) (KSATMIN) | 100 b | 20 b | 2 b | 1 b | 0.5 b |
| Conductivity at macro/micropore boundary (mm/hr) (KSM) | 0.05 b | 0.05 b | 0.05 b | 0.05 b | 0.05 b |
| FIELD DRAINAGE |  |  |  |  |  |
| Drain depth (m) (DRAINDEP) | 0.55 a |
| Drain spacing (m) (SPACE) | 2.0 a |
| Transmission coefficient at bottom boundary (h-1) (BGRAD) | 1.0 x 10-6 c |

a derived from measured values or known.

b calibrated.

c default or assumed value.

d derived from pedo-transfer function.

Table C.13. Scenario-specific soil and site parameters for D3

| Horizon designation (FAO, 1990) | Ap | Bw | C |
| --- | --- | --- | --- |
| Depth (cm) | 0-30 | 30-50 | 50-175 |
| BASIC PROPERTIES |  |  |  |
| Sand (%) | 91 | 93 | 96 |
| Silt (%) | 6 | 4 | 2 |
| Clay (%) | 3 | 3 | 2 |
| Texture (FAO, 1990; USDA, 1999) | sand | sand | Sand |
| Organic carbon (%) | 2.3 | 0.5 | 0.1 |
| Bulk density (g/cm3) (GAMMA) | 1.35 a | 1.46 a | 1.67 a |
| PH | 5.3 | 5.1 | 4.7 |
| Soil structure (FAO, 1990) | single grain | single grain | single grain |
| HYDRAULIC PROPERTIES |  |  |  |
| Saturated water content (%) (TPORV) | 48 a | 44 a | 36 a |
| Wilting point (%) (WILT) | 6 a | 6 a | 6 a |
| Residual water content (%) (RESID) | 3 a | 3 a | 3 a |
| Water content at macro/micropore boundary (%) (XMPOR) | 37 a | 29 a | 29 a |
| Water tension at macro/micropore boundary (cm) (CTEN) | 39 a | 45 a | 45 a |
| Pore-size distribution index (ZLAMB) | 0.847 a | 1.958 a | 1.958 a |
| Tortuosity factor micropores (ZM) | 0.5 a | 0.5 a | 0.5 a |
| Tortuosity factor macropores (ZN) | 4 c | 4 c | 4 c |
| Effective diffusion pathlength (mm) (ASCALE) | 20 c | 1 c | 1 c |
| Saturated hydraulic conductivity (mm/hr) (KSATMIN) | 70 a | 110 a | 110 a |
| Conductivity at macro/micropore boundary (mm/hr) (KSM) | 0.54 a | 1.9 a | 1.9 a |
| FIELD DRAINAGE |  |  |  |
| Drain depth (m) (DRAINDEP) | 1.75 a |
| Drain spacing (m) (SPACE) | 76.0 a |
| Transmission coefficient at bottom boundary (h-1) (BGRAD) | 0.0 c |

a derived from measured values or known.

c default or assumed value.

Table C.14. Scenario-specific soil and site parameters for D4

| Horizon designation (FAO, 1990) | Ap | Eb | Ebg | Btg | BCg |
| --- | --- | --- | --- | --- | --- |
| Depth (cm) | 0-25 | 25-45 | 45-75 | 75-120 | 120-180 |
| BASIC PROPERTIES |  |  |  |  |  |
| Sand (%) | 51 | 70 | 67 | 33 | 73 |
| Silt (%) | 37 | 17 | 18 | 39 | 17 |
| Clay (%) | 12 | 13 | 15 | 28 | 10 |
| Texture (FAO, 1990; USDA, 1999) | loam | Sandy loam | Sandy loam | Clay loam / loam | Sandy loam |
| Organic carbon (%) | 1.4 | 0.8 | 0.3 | 0.2 | 0.1 |
| Bulk density (g/cm3) (GAMMA) | 1.48 a | 1.65 a | 1.65 a | 1.76 a | 1.80 a |
| PH | 6.9 | 7.1 | 7.2 | 7.5 | 7.5 |
| Soil structure (FAO, 1990) | weak medium subangular blocky | weak medium subangular blocky | weak medium subangular blocky | moderate coarse subangular blocky | Weak coarse subangular blocky |
| HYDRAULIC PROPERTIES |  |  |  |  |  |
| Saturated water content (%) (TPORV) | 42 a | 36 a | 36 a | 33 a | 30 c |
| Wilting point (%) (WILT) | 15 a | 13 a | 13 a | 16 a | 13 c |
| Residual water content (%) (RESID) | 4 a | 4 a | 4 a | 3 a | 3 c |
| Water content at macro/micropore boundary (%) (XMPOR) | 40 a | 34 a | 34 a | 32 a | 29 c |
| Water tension at macro/micropore boundary (cm) (CTEN) | 10 c | 12 c | 12 c | 16 c | 16 c |
| Pore-size distribution index (ZLAMB) | 0.15 a | 0.15 a | 0.15 a | 0.15 a | 0.12 |
| Tortuosity factor micropores (ZM) | 0.5 c | 0.5 c | 0.5 c | 0.5 c | 0.5 c |
| Tortuosity factor macropores (ZN) | 3 b | 3 b | 3 b | 3 b | 3 b |
| Effective diffusion pathlength (mm) (ASCALE) | 55 b | 55 b | 55 b | 55 b | 55 b |
| Saturated hydraulic conductivity (mm/hr) (KSATMIN) | 30 a | 15 a | 8 a | 1 a | 0.2 a |
| Conductivity at macro/micropore boundary (mm/hr) (KSM) | 0.5 a | 1.0 b | 0.7 b | 0.1 b | 0.1 b |
| FIELD DRAINAGE |  |  |  |  |  |
| Drain depth (m) (DRAINDEP) | 1.2 a |
| Drain spacing (m) (SPACE) | 10.0 b |
| Transmission coefficient at bottom boundary (h-1) (BGRAD) | 3 x 10-6 b |

a derived from measured values or known.

b calibrated.

c default or assumed value.

Table C.15. Scenario-specific soil and site parameters for D5

| Horizon designation | Ap | Bg | BCg |
| --- | --- | --- | --- |
| Depth (cm) | 0-25 | 25-60 | 60-90 |
| BASIC PROPERTIES |  |  |  |
| Sand (%) | 42 | 38 | 59 |
| Silt (%) | 39 | 35 | 19 |
| Clay (%) | 19 | 27 | 22 |
| Texture (FAO, 1990; USDA, 1999) | loam | loam | Sandy clay loam |
| Organic carbon (%) | 2.1 | 0.8 | 0.2 |
| Bulk density (g/cm3) (GAMMA) | 1.55 a | 1.63 a | 1.70 a |
| pH | 6.5 | 7.0 | 4.9 |
| Soil structure (FAO, 1990) | moderate medium subangular blocky | weak coarse subangular blocky | weak coarse subangular blocky |
| HYDRAULIC PROPERTIES |  |  |  |
| Saturated water content (%) (TPORV) | 41 d | 38 d | 36 d |
| Wilting point (%) (WILT) | 18 d | 21 d | 17 d |
| Residual water content (%) (RESID) | 0 d | 0 d | 0 d |
| Water content at macro/micropore boundary (%) (XMPOR) | 39 d | 36 d | 32 d |
| Water tension at macro/micropore boundary (cm) (CTEN) | 12 d | 13 d | 11 d |
| Pore-size distribution index (ZLAMB) | 0.106 d | 0.082 d | 0.088 d |
| Tortuosity factor micropores (ZM) | 0.5 d | 0.5 d | 0.5 d |
| Tortuosity factor macropores (ZN) | 4 d | 4 d | 4 d |
| Effective diffusion pathlength (mm) (ASCALE) | 20 d | 25 d | 25 d |
| Saturated hydraulic conductivity (mm/hr) (KSATMIN) | 30 d | 28 d | 13 d |
| Conductivity at macro/micropore boundary (mm/hr) (KSM) | 0.25 d | 0.16 d | 0.20 d |
| FIELD DRAINAGE |  |  |  |
| Drain depth (m) (DRAINDEP) | 0.9 c |
| Drain spacing (m) (SPACE) | 9 c |
| Transmission coefficient at bottom boundary (h-1) (BGRAD) | 0.0 c |

a derived from measured values or known.

c default or assumed value.

d derived from pedo-transfer function.

Table C.16. Scenario-specific soil and site parameters for D6

| Horizon designation | Ap | Bw | Bw(g) | BCg |
| --- | --- | --- | --- | --- |
| Depth (cm) | 0-30 | 30-60 | 60-90 | 90-165 |
| BASIC PROPERTIES |  |  |  |  |
| Sand (%) | 36 | 37 | 29 | 27 |
| Silt (%) | 34 | 34 | 34 | 27 |
| Clay (%) | 30 | 29 | 37 | 46 |
| Texture (FAO, 1990; USDA, 1999) | Clay loam | Clay loam | Clay loam | Clay |
| Organic carbon (%) | 1.2 | 0.6 | 0.4 | 0.3 |
| Bulk density (g/cm3) (GAMMA) | 1.43 d | 1.37 d | 1.55 d | 1.59 d |
| PH | 7.5 | 7.5 | 7.5 | 7.5 |
| Structure (FAO, 1990) | Moderate medium subangularblocky | Moderate medium subangular blocky | Moderate coarse prismatic | Weak medium angular blocky |
| HYDRAULIC PROPERTIES |  |  |  |  |
| Saturated water content (%) (TPORV) | 45 d | 48 d | 41 d | 40 d |
| Wilting point (%) (WILT) | 23 d | 22 d | 24 d | 25 d |
| Residual water content (%) (RESID) | 0 d | 0 d | 0 d | 0 d |
| Water content at macro/micropore boundary (%) (XMPOR) | 42 d | 43 d | 39 d | 39 d |
| Water tension at macro/micropore boundary (cm) (CTEN) | 12 d | 12 d | 14 d | 16 d |
| Pore-size distribution index (ZLAMB) | 0.086 d | 0.090 d | 0.071 d | 0.063 d |
| Tortuosity factor micropores (ZM) | 0.5 d | 0.5 d | 0.5 d | 0.5 d |
| Tortuosity factor macropores (ZN) | 3 d | 3 d | 2 d | 2 d |
| Effective diffusion pathlength (mm) (ASCALE) | 50 d | 20 d | 100 d | 10 d |
| Saturated hydraulic conductivity (mm/hr) (KSATMIN) | 100 d | 40 d | 10 d | 5 d |
| Conductivity at macro/micropore boundary (mm/hr) (KSM) | 0.2 d | 0.2 d | 0.2 d | 0.1 d |
| FIELD DRAINAGE |  |  |  |  |
| Drain depth (m) (DRAINDEP) | 1.0 c |
| Drain spacing (m) (SPACE) | 8.0 c |
| Transmission coefficient at bottom boundary (h-1) (BGRAD) | 3.0 x 10-6 c |

c default or assumed value.

d derived from pedo-transfer function.

## Table C.17. Numerical layer thicknesses for the drainage scenarios

| Scenario | Layer thicknesses (cm), top layer to bottom |
| --- | --- |
| D1 | 3,4,5,8,10,10,10,10,10,15,15,15,20,20,20 |
| D2 | 3,6,6,5,10,5,5,10,10,5,10,15,10,20,30 |
| D3 | 3,4,5,8,10,10,10,10,10,15,15,15,20,20,20 |
| D4 | 3,5,6,6,5,5,5,10,15,15,10,15,20,30,30 |
| D5 | 2,4,4,5,5,5,5,5,5,5,5,10,10,10,10 |
| D6 | 3,6,6,7,8,10,10,10,10,10,10,10,20,20,25 |