Test results for FOCUS_TOXSWA_1.1.1

Standard drainage and runoff input files are used to test the new TOXSWA version. These are:

- 6 *.m2t files and 4 *.p2t files,

- representing output for 3 applications of 1 kg/ha

- of FOCUS Compound D_sw

- to winter cereals (maize for R2)

- with the first appln at the day around emergence (appln window for PAT: emergence-5 up to emergence+50 d,

- appln interval 6 d,

- application method: ground spray).

They can be found at the home page of the workgroup. The *.m2t and *.p2t file need to be copied into the corresponding SWASHprojects folder for MACRO and PRZM, respectively. Change the runid’s of these files to the runid’s necessary for running TOXSWA (see the exact path in the corresponding txw input file).

These ‘average’ drainage and runoff fluxes are coupled to a less and a more persistent compound in water, respectively FOCUS Compound A_sw and H_sw.

So create 2 projects in SWASH with:

- compound A_sw and compound H_sw

- winter cereals (maize for R2)

- 3 applications of 1 kg/ha

- with the first appln at the day around emergence (appln window for PAT: emergence-5 up to emergence+50 d,

- appln interval 6 d

- application method: ground spray

1.  Model output for 3 applications of 1 kg/ha of FOCUS Compound A_sw to winter cereals (maize for R2) with the first appln at the day around emergence

| Scenario Executed at 24-Apr-2003 | Appln date (not changed) | Water | Sediment |
| --- | --- | --- | --- |
|  |  | Global max (μg/L) [Date] | TWAC 28 d (μg/L) | Global max (μg/L) [Date] |
| D1-Ditch | 3-Oct-1982 23-Oct-1982 5-Nov-1982 | 225.322 22-Nov-1982 | 144.921 | 57.592 25-Nov-1982 |
| D1-Stream | 3-Oct-1982 23-Oct-1982 5-Nov-1982 | 157.715 13-Nov-1982 | 100.997 | 39.094 25-Nov-1982 |
| D2-Ditch | 3-Nov-1986 28-Nov-1986 8-Dec-1986 | 466.838 12-Dec-1986 | 156.592 | 69.059 15-Dec-1986 |
| D2-Stream | 3-Nov-1986 28-Nov-1986 8-Dec-1986 | 333.303 11-Dec-1986 | 102.087 | 44.020 15-Dec-1986 |
| D3-Ditch | 22-Nov-1992 28-Nov-1992 10-Dec-1992 | 29.885 22-Nov-1992 | 25.777 | 8.797 10-Dec-1992 |
| D4-Pond | 28-Sep-1985 4-Oct-1985 26-Oct-1985 | 31.201 21-Dec-1985 | 23.758 | 9.366 23-Dec-1985 |
| D4-Stream | 28-Sep-1985 4-Oct-1985 26-Oct-1985 | 102.111 9-Dec-1985 | 75.326 | 26.290 21-Dec-1985 |
| D5-Pond | 27-Nov-1978 18-Dec-1978 01-Jan-1979 | 42.088 12-Feb-1979 | 18.308 | 9.965 14-Feb-1979 |
| D5-Stream | 27-Nov-1978 18-Dec-1978 01-Jan-1979 | 70.481 11-Feb-1979 | 40.855 | 17.582 13-Feb-1979 |
| D6-Ditch | 6-Dec-1986 30-Dec-1986 14-Jan-1987 | 156.174 19-Jan-1987 | 26.258 | 15.289 19-Jan-1987 |
| R1-Pond | 14-Nov-1978 20-Nov-1978 27-Nov-1978 | 1.100 25-Nov-1978 | 0.251 | 0.163 28-Nov-1978 |
| R1-Stream | 14-Nov-1978 20-Nov-1978 27-Nov-1978 | 92.865 25-Nov-1978 | 1.487 | 5.628 25-Nov-1978 |
| R2-Stream | 26-Apr-1977 7-May-1977 20-May-1977 | 35.806 13-May-1977 | 1.031 | 2.844 13-May-1977 |
| R3-Stream | 5-Dec-1980 11-Dec-1980 20-Dec-1980 | 161.811 16-Dec-1980 | 4.679 | 10.440 16-Dec-1980 |
| R4-Stream | 5-Nov-1979 10-Dec-1979 24-Dec-1979 | 10.770 21-Dec-1979 | 0.246 | 0.758 21-Dec-1979 |

2. Model output for 3 applications of 1 kg/ha of FOCUS Compound H_sw to winter cereals (maize for R2) with the first appln at the day around emergence

| Scenario Executed at 24-Apr-2003 | Appln date (not changed) | Water | Sediment |
| --- | --- | --- | --- |
|  |  | Global max (μg/L) [Date] | TWAC 28 d (μg/L) | Global max (μg/L) [Date] |
| D1-Ditch | 3-Oct-1982 23-Oct-1982 5-Nov-1982 | 247.080 20-Nov-1982 | 164.868 | 222.853 27-Nov-1982 |
| D1-Stream | 3-Oct-1982 23-Oct-1982 5-Nov-1982 | 158.426 13-Nov-1982 | 102.142 | 126.212 27-Nov-1982 |
| D2-Ditch | 3-Nov-1986 28-Nov-1986 8-Dec-1986 | 470.648 12-Dec-1986 | 175.087 | 259.757 31-Dec-1986 |
| D2-Stream | 3-Nov-1986 28-Nov-1986 8-Dec-1986 | 333.837 11-Dec-1986 | 102.840 | 153.175 31-Dec-1986 |
| D3-Ditch | 22-Nov-1992 28-Nov-1992 10-Dec-1992 | 33.141 22-Nov-1992 | 30.045 | 88.788 11-Jan-1993 |
| D4-Pond | 28-Sep-1985 4-Oct-1985 26-Oct-1985 | 127.148 31-Jan-1986 | 123.287 | 286.989 5-Apr-1986 |
| D4-Stream | 28-Sep-1985 4-Oct-1985 26-Oct-1985 | 102.289 9-Dec-1985 | 75.577 | 110.523 30-Jan-1986 |
| D5-Pond | 27-Nov-1978 18-Dec-1978 01-Jan-1979 | 110.733 17-Feb-1979 | 106.091 | 232.186 1-May-1979 |
| D5-Stream | 27-Nov-1978 18-Dec-1978 01-Jan-1979 | 70.554 11-Feb-1979 | 41.027 | 72.715 11-Apr-1979 |
| D6-Ditch | 6-Dec-1986 30-Dec-1986 14-Jan-1987 | 157.164 19-Jan-1987 | 28.957 | 58.944 20-Jan-1987 |
| R1-Pond | 14-Nov-1978 20-Nov-1978 27-Nov-1978 | 1.462 27-Nov-1978 | 1.281 | 1.845 2-Feb-1979 |
| R1-Stream | 14-Nov-1978 20-Nov-1978 27-Nov-1978 | 93.610 25-Nov-1978 | 1.508 | 12.218 25-Nov-1978 |
| R2-Stream | 26-Apr-1977 7-May-1977 20-May-1977 | 36.198 13-May-1977 | 1.047 | 6.500 13-May-1977 |
| R3-Stream | 5-Dec-1980 11-Dec-1980 20-Dec-1980 | 163.022 16-Dec-1980 | 4.774 | 22.984 16-Dec-1980 |
| R4-Stream | 5-Nov-1979 10-Dec-1979 24-Dec-1979 | 10.816 21-Dec-1979 | 0.249 | 1.662 21-Dec-1979 |

# Footnotes

Please note that these runs are intended as a test for the TOXSWA software only. They do not correspond to sensible, consistent step 3 FOCUS runs that can be used for risk assessment purposes. (E.g. because PRZM and MACRO do calculations for a pesticide with D-sw properties, while TOXSWA performs calculations for a pesticide with A-sw or H-sw properties.)