Version: 1.0

Date: 2/4/01

MACRO - Parameterisation for the FOCUS Groundwater Scenarios

About this document

The report on which this document is based is that of the FOCUS Groundwater Scenarios workgroup, which is an official guidance document in the context of 91/414/EEC [full citation is FOCUS (2000) “FOCUS groundwater scenarios in the EU review of active substances” Report of the FOCUS Groundwater Scenarios Workgroup, EC Document Reference SANCO/321/2000 rev.2, 202pp].  This document does not replace the official FOCUS report.  However, a need was identified to maintain the parameterisation of the models for the FOCUS groundwater scenarios in an up-to-date version controlled document, as changes become necessary.  That is the purpose of this document.

Summary of changes made since the official FOCUS Groundwater Scenarios Report (SANCO/321/2000 rev.2).

New in Version 1.0

The only changes in this version compared with the original report are editorial ones.

## Summary

MACRO 4.2 is a one-dimensional, non-steady state model of water flow and solute transport in a layered soil at the pedon/ field scale. The model describes a high-conductivity/low porosity macropore domain coupled to a low-conductivity/high porosity domain representing the soil matrix. Mass exchange between the domains is calculated with approximate, yet physically based, first order expressions. The model structure therefore enables quantitative evaluation of the impact of water flow and solute transport through macropores in structured soil. However, types of preferential flow other than through macropores are not simulated.

With respect to the FOCUS groundwater scenarios, MACRO was parameterised for the Châteaudun scenario only. MACRO includes the following processes:

| - | Unsaturated water flow | Richards’ equation in micropores, gravity flow in macropores |
| --- | --- | --- |
| - | Root water uptake | Empirical sink term, water preferentially extracted from macropores |
| - | Seepage to drains | Seepage potential theory. Sink term in the vertical water flow equation. Drains are not simulated for the FOCUS groundwater scenarios. |
| - | Solute transport | Convection/dispersion equation in the micropores, mass flow only in the macropores |
| - | Mass exchange | Approximate first order rate equation for mass exchange of both solute and water |
| - | Sorption | Instantaneous equilibrium, Freundlich isotherm, sorption partitioned between micro- and macropores |
| - | Degradation | First-order kinetics, separate rate coefficients for four pools (solid and liquid, micro- and macropores). |
| - | Metabolism | One metabolite can be simulated at a time |
| - | Canopy interception and washoff | These routines are turned off, following FOCUS procedures. |
| - | Plant uptake | Plant uptake is calculated as a function of plant transpiration |

MACRO does not (or not fully) include the following processes

| - | Volatilisation | A lumped dissipation rate including volatilisation, photolysis etc. may be given for the leaves, but this option is not active in the FOCUS scenarios. Volatilisation from the soil is not included. |
| --- | --- | --- |
| - | Surface runoff | Surface runoff of water and solute is only included in the sense that if the surface layer is saturated, the excess water and solute is lost to the profile. But it cannot be used to model runoff processes as such. |

The main issues encountered during parameterisation were :

- the transformation of the van Genuchten parameters (Table 1) which were given for the profile to Brooks-Corey parameters for the soil matrix. Both parameter sets were derived from measured data. Effectively the soil parameters used in the simulations are almost identical to those used by the other models. The resulting parameters are listed in Table 2.

- the parameterisation of macropore flow. The relevant parameters were given values based partly on the pedotransfer functions available in MACRO_DB, and partly on a rough calibration of the model on measured water flow data from lysimeters at Chateaudun (Villamblain). In the Chateaudun profile, macropore flow is assumed to be weak in the upper 25cm, strong between 25 and 60cm depth, and non-existent below 60cm.

In addition to the crop parameters specifically given for the FOCUS scenarios, a number of crop parameters had to be estimated. This concerns, among others, LAI at harvest, a root adaptability factor, maximum water interception by the crop, factors describing the change in leaf area development over time, critical soil air content for root water uptake, a factor describing the distribution of the roots in the root zone, critical tension for root water uptake, and a correction factor for evaporation from wet canopy. The parameter set for the crops grown at Chateaudun is listed in Tables 3 and 4.

The reduction of substance reaching the soil surface due to crop interception is parameterised as follows. The user should input the dose actually reaching the ground, excluding the amount intercepted by the crop.  The fraction intercepted is determined from the interception tables as described in the guidelines in Chapter 2.3 of the FOCUS report. Washoff is set to zero ensuring that only the amount of substance directly entering the soil contributes to leaching.

## Introduction

A common shell program has been written for the MACRO model to run the single FOCUS groundwater scenario as well as the six FOCUS surface water scenarios being developed for MACRO. The shell program is PC-based and written in Visual Basic. All parameter values defining the scenarios are contained in a number of Microsoft Access databases. For the single groundwater scenario at Châteaudun, the user simply selects a crop from the available list, and then sets options for the length of simulation (20, 40 or 60 years), and whether or not macropore flow and irrigation are to be simulated (in the latter case, for those crops which may be irrigated). Substance properties can also be defined interactively and stored in a separate database for later use. In-built calculation and plot routines present the results of the simulations to the user in the correct format for FOCUS, both in tables and figures.

The scenario and parameter definitions are based on:

- FOCUS DEFINITION = General definitions made by the FOCUS working group

- FOCUS SCENARIO SPECIFIC = Definitions made by the FOCUS working group for a specific scenario

- DEVELOPMENT DEFINITION = Definitions made by the FOCUS working group specifically for the MACRO model.

- USER INPUT = Input defined by the user, through choices and selections made in the MACRO shell.

The shell program creates a parameter file (ASCII file, with extension .par) based on the selections of the user. This parameter file is described below in detail, in case users wish to make subsequent use of these files for higher tier assessments, by modifying them, and running simulations with MACRO DOS 4.2.

For metabolite simulations, a separate .par file is created, and the output file from the simulation of the mother substance is used as input to the metabolite simulation.

## Input files

The meteorological files are stored as binary formatted (.bin extension) files. They contain the following information:

| Parameter and description | Value, source & comments |
| --- | --- |
| Rainfall file | czm6p.bin |  |
|  | Date | FOCUS SCENARIO SPECIFIC |
|  | Precipitation (mm day-1) | FOCUS SCENARIO SPECIFIC |
| Evaporation file | czm6et.bin |  |
|  | Date | FOCUS SCENARIO SPECIFIC |
|  | Potential evaporation (mm day-1) | FOCUS SCENARIO SPECIFIC |
|  | Max daily temperature, (°C) | FOCUS SCENARIO SPECIFIC |
|  | Min. daily temperature, (°C) | FOCUS SCENARIO SPECIFIC |

## Switches

Values of switches (= options) determine the type of simulation to be performed and the parameters required.

Technical Switches

| Parameter and description | Value, source & comments |
| --- | --- |
| Averagex | Determines whether the output value is calculated as the value at the end of the interval (1) or the average value of a variable for a calculation interval (2). | 2 is chosen. DEVELOPMENT DEFINITION. |
| Chapar | Allows the use of more than one parameter set during a simulation. | For most of the crops, one parameter set is chosen (OFF). However, for the crop with two growing seasons during the year, the switch is ON. DEVELOPMENT DEFINITION for each crop choice based on the FOCUS scenarios. |
| Driving | Specifies whether metabolites are being simulated | For all simulations without metabolites it is set to 0. For simulation of a metabolite, it is set to 1. USER INPUT. |
| Lisallv | General selection of output variables to summary file | All possible output variables are written to the summary file (2). DEVELOPMENT DEFINITION |
| Metabolite | Specifies whether a driving file for metabolites is to be produced. | This parameter is set to OFF if no metabolites of a certain substance are to be simulated. If metabolites are to be simulated, it is set to ON. When simulating the metabolite (Driving=1), it is set to OFF. USER INPUT |
| Validpg | Specifies whether there is comparison with measured data | As there is no comparison with measured data, this parameter is set to 0. DEVELOPMENT DEFINITION. |

Model Specific Switches

| Parameter and description | Value, source & comments |
| --- | --- |
| Boundary | Specifies the lower boundary condition for the column. | The groundwater depth is FOCUS SCENARIO SPECIFIC, the exact choice of lower boundary condition is a DEVELOPMENT DEFINITION. MACRO allows five different lower boundary conditions, namely 1) unit hydraulic gradient, 2) flux as an empirical function of water table height; 3) water table in the soil profile, 4) constant potential, and 5) lysimeter with free drainage. Due to the fact that the groundwater is at 12 m depth at Chateaudun, the constant potential gradient is selected as lower boundary condition. |
| Crop | Indicates the type of cover. The model allows bare soil conditions (1), annual crops (2), or perennial crops (3). | FOCUS SCENARIO SPECIFIC. The parameter is set to 2 or 3 depending on the crop. |
| Evaporate | Indicates the type of input given for calculation of potential evaporation. | As daily potential evaporation is given as input to the model, the value is set to 1. DEVELOPMENT DEFINITION. |
| Initial | Indicates which type of initial condition for water content is selected. | The initial condition is set as an equilibrium profile (1). Due to the six years of warming up period used in the simulations, the values are not critical for the simulation. |
| Irrigate | Indicates whether or not irrigation should be treated as rainfall. | As the substance is given as an irrigation, irrigation should be treated separately from rainfall (1). DEVELOPMENT DEFINITION. |
| Massunits | Allows selection of different mass units. | The units mg are selected as mg m-3 equals mg l-1, which is an appropriate unit for the substance simulations. DEVELOPMENT DEFINITION |
| Rainfall | Specifies the type of rainfall record. | As daily rainfall is used, this parameter is set to 1. DEVELOPMENT DEFINITION. |
| Solute | Specifies the solute being simulated. | MACRO allows simulation of water and heat, pesticide, non-reactive solute or tritium. The parameter should be set to 2. DEVELOPMENT DEFINITION. |
| Tiledrain | Indicates presence or absence of tile drains. | As no tile drains are present in the Châteaudun scenario, this parameter is set to 2. (FOCUS SCENARIO SPECIFIC parameter). |

## 5 Parameters

### Soil profile

| Parameter and description | Value, source & comments |
| --- | --- |
| Nlayer | Number of layers to be simulated (max 22) | Set to 15 - DEVELOPMENT DEFINITION |
| Z(1-15) | Thickness in mm of the 15 layers | The division between the layers is chosen on the basis that i) a horizon should preferably contain at least 3 layers, ii) the top layers should be thinner than 5 cm, to avoid numerical dispersion, the layers should not exceed 10 cm, since the dispersivity is set to 5 cm the division between layers should equal the division between horizons below 1 m, an attempt was made to extend the depth as much as possible (violating criteria iii above) The fact that the layers are thicker than 10 cm below 1 m depth means that dispersion is overestimated. This will overestimate leaching to depths greater than 1 m. Despite this, results up to 1.9 m depth are considered acceptable at a higher tier, because the additional dispersion is conservative in its effect. (DEVELOPMENT DEFINITION) |
|  |  | The final division at Châteaudun was |
|  |  | Horizon | Layers, mm | Final depth, cm |
|  |  | 1 | 20+60+80+90 | 25 |
|  |  | 2 | 80+90+80 | 50 |
|  |  | 3 | 100 | 60 |
|  |  | 4 | 100+100+100+100 | 100 |
|  |  | 5 | 200 | 120 |
|  |  | 6 | 300+400 | 190 |

### Site

| Parameter and description | Value, source & comments |
| --- | --- |
| ANNAMP | The temperature amplitude between the average temperature in January and July. (°C) | Calculated from the weather record to be 7.7 oC. FOCUS SCENARIO SPECIFIC. |
| ANNTAV | The average annual temperature (°C) | Calculated from the weather record to be 11. 9 oC. FOCUS SCENARIO SPECIFIC. |
| PHI | Site latitude | 48.1 (FOCUS SCENARIO SPECIFIC) |
| RAINCO | Correction coefficient for rain. | For the scenarios it is assumed to be 1. DEVELOPMENT DEFINITION |
| RINTEN | A typical rainfall intensity for the area in question (mm hr-1). | For southern England, a value of 2 mm/hr is realistic. The same value was selected for Chateaudun. DEVELOPMENT DEFINITION |
| SNOWCO | Correction factor for snowfall. | For the scenarios it is assumed to be 1. DEVELOPMENT DEFINITION. |
| SNOWMF | This factor governs the rate of snowmelt. | Set to default, 4.5 mm degree-1 day-1. Snow is not regarded to be important in Chateaudun. DEVELOPMENT DEFINITION. |

### Initial/Boundary conditions

| Parameter and description | Value, source & comments |
| --- | --- |
| BOTEN | Tension at the lower boundary of the profile (cm) | For groundwater at 12 m depth as defined for Chateaudun, the value is calculated as (12 – 1.9 m = 10.1 m), assuming equilibrium conditions. The resulting tension at the bottom of the soil column is 1010 cm. DEVELOPMENT DEFINITION based on FOCUS SCENARIO SPECIFIC parameters. |
| CONCIN | Solute concentration at the bottom boundary | Set to zero (FOCUS DEFINITION) |
| SOILINIT | Initial concentration in the soil | Set to zero (FOCUS DEFINITION) |
| TEMPINI | Initial temperature in the soil profile. | Set to 10 °C. Due to the warming up period, the initial values are without importance for the simulation. DEVELOPMENT DEFINITION. |

### Solute transport

| Parameter and description | Value, source & comments |
| --- | --- |
| AEXC | Excluded volumetric water content due to anion exclusion. (%) | Set to zero. DEVELOPMENT DEFINITION. |
| CONC | The solute concentration in rainfall | Set to zero. FOCUS DEFINITION |
| DIFF | The diffusion coefficient for the substance (m2 s-1) | USER INPUT. The default value is 5.0 E-10. |
| DV | Dispersivity (cm) | Set to 5 cm – FOCUS DEFINITION |
| FSTAR | The solute concentration factor for crop uptake of substance | USER INPUT. The default value is 0.5 |
| ZMIX | Mixing depth for rainfall and soil moisture (mm). | Set to 1 mm (default). DEVELOPMENT DEFINITION. |

### Substance

| Parameter and description | Value, source & comments |
| --- | --- |
| CANDEG | Dissipation rate coefficient on leaves (1/days) | 0.2 (default value). This is irrelevant since the crop interception is set to zero (FOCUS DEFINITION) |
| DEGMAL | Degradation rate coefficient (1/days), at a moisture content of XMPOR and the temperature TREF, for the liquid phase in the macropores | USER INPUT for each layer. Although MACRO internally uses XMPOR as the reference moisture for degradation, it has been ensured through the shell that the degradation value at pF2 is exactly equal to that used in the other FOCUS models. |
| DEGMAS | As above, for the solid phase in the macropores | USER INPUT, for each layer. |
| DEGMIL | As above, for the liquid phase in the micropores. | USER INPUT, for each layer. |
| DEGMIS | As above, for the solid phase of the micropores. | USER INPUT, for each layer. |
| EXPB | Exponent of moisture corrected degradation (moisture relationship according to WALKER) | USER INPUT (0.7 = default value) |
| FCONVERT | Fraction of degraded parent compound converted to metabolite. | USER INPUT. |
| FEXT | Wash-off coefficient for the leaves (1/mm) | Set to zero. Irrelevant. FOCUS DEFINITION. |
| FRACMAC | The fraction of sorption sites in the macropores | 0.02 (default value in model) DEVELOPMENT DEFINITION. |
| FREUND | Exponent of the Freundlich isotherm | USER INPUT |
| TREF | Reference temperature for substance degradation (oC) | USER INPUT |
| TRESP | Exponent in the temperature response function (1/Kelvin) | USER INPUT (default value = 0.079) |
| ZKD | Sorption distribution coefficient, cm3 g-1 | USER INPUT |

### Physical/Hydraulic properties

For the hydraulic parameters, the parameterisation of MACRO is different from the other models. The hydraulic parameters (retention curve and unsaturated hydraulic conductivity) were fitted both with the van Genuchten/Mualem and Brooks-Corey/Mualem models. The two fits produce very similar results for the micro-pore range of tensions, but rather different results near saturation. All required data are listed in Tables 1 and 2.

| Parameter and description | Value, source & comments |
| --- | --- |
| ASCALE | Effective diffusion pathlength (mm) | Determined via the pedotransfer functions in MACRO DB, based on the description of soil structure. The values chosen are 10 (0-25 cm), 75 (25-60 cm), 1 (60-120 cm) and 4 (120-190 cm). DEVELOPMENT DEFINITION |
| CTEN | Tension defining the macropore- micropore boundary (cm) | DEVELOPMENT DEFINITION The value may be identified from measured unsaturated hydraulic conductivity curves, as the point where the curve „breaks“. The Villamblain data did not cover the tension range close to saturation. The values were chosen to give 1) a good fit to the unsaturated conductivity, with 2) a value as close to saturation as possible (if CTEN moves too far away from saturation, the model assumption of gravity flow in macropores breaks down. The value is given as hb in the Table 2. |
| GAMMA | Bulk density (g/cm3) | FOCUS SCENARIO SPECIFIC |
| KSATMIN | The saturated hydraulic conductivity (mm hr-1) | Given in Table 1 as Ksat for Chateaudun. FOCUS SCENARIO SPECIFIC. |
| KSM | The saturated hydraulic conductivity of the micropores (mm hr-1) | Kb in Table 2. DEVELOPMENT DEFINITION |
| RESID | Residual moisture content (%) | Given in Table 1 as qr for Chateaudun. FOCUS SCENARIO SPECIFIC. |
| TPORV | Saturated water content (%) | Given in Table 1 as qs for Chateaudun. FOCUS SCENARIO SPECIFIC. |
| WILT | Wilting point (%) | FOCUS SCENARIO SPECIFIC, but slightly changed due to the fact that MACRO requires Brooks- Corey parameters. Given in Table 2 as water content at 1600kPa for Chateaudun. |
| XMPOR | Saturated water content of micropores (%) | qb in Table 2. DEVELOPMENT DEFINITION. |
| ZA | Parameter relevant for simulation of shrinkage | Set to 1. Irrelevant for the simulation |
| ZLAMB | Pore size distribution index | b in Table 2. DEVELOPMENT DEFINITION |
| ZM | Tortuosity factor, micropores | ( in Table 2. DEVELOPMENT DEFINITION. |
| ZN | Tortuosity factor, macropores | The value of ZN was chosen based on a very approximate calibration against measured water discharges from the Villamblain lysimeters. A value of 3.0 is selected down to 60 cm, 2 in the deeper layers. DEVELOPMENT DEFINITION |
| ZP | Indicates presence or absence of shrinkage | Set to 0 = no shrinkage. DEVELOPMENT DEFINITION. |

### Crop

Crop parameters at Chateaudun are listed in Tables 3 and 4.

| Parameter and description | Value, source & comments |
| --- | --- |
| BETA | Root adaptability factor | DEVELOPMENT DEFINITION for each crop. |
| CANCAP | Maximum water interception by the crop (mm) | CANCAP may be calculated as approximately 0.5 * LAI max. However, in some cases, values were selected to match the FOCUS surface water scenarios. DEVELOPMENT DEFINITION. |
| CFORM | Leaf development form factor for the period from emergence to maturity | The values given in Table 3 are derived from visual comparisons between published growth curves and fitted curves. DEVELOPMENT DEFINITION. |
| CRITAIR | Critical soil air content for root water uptake (%) | Kept at default (= 5). This value is not too far from the difference between field capacity and saturation weighted through the first meter of the profile, and also the default value used for the FOCUS surface water group. DEVELOPMENT DEFINITION. |
| DFORM | Leaf senescence form factor for the period from maturity to harvest | The values given in Table 3 are derived from visual comparisons between published growth curves and fitted curves. DEVELOPMENT DEFINITION. |
| IDMAX | The day of maturity of the crop | FOCUS SCENARIO SPECIFIC |
| IDSTART | The day of emergence of the crop | FOCUS SCENARIO SPECIFIC |
| IDHARV | The day of harvest of the crop | FOCUS SCENARIO SPECIFIC |
| LAIHARV | LAI at harvest | The values given in Table 3 are derived from published data. DEVELOPMENT DEFINITION |
| LAIMAX | LAI at maturity | FOCUS SCENARIO SPECIFIC |
| LAIMIN | The LAI at the date ZDATEMIN | For spring-sown crops the value is close to zero, for winter crops it is the LAI value during early spring. DEVELOPMENT DEFINITION. |
| ROOTINIT | The root depth at the date ZDATEMIN (m). | Set to the values given in Table 3. For summer crops the value is close to zero, for winter crops it is the root depth during early spring. DEVELOPMENT DEFINITION. |
| ROOTMAX | Maximum root depth, m. | FOCUS SCENARIO SPECIFIC. |
| RPIN | Percentage of the root length in the top 25 % of the root depth. | Set to 60 % (model default). DEVELOPMENT DEFINITION. |
| WATEN | Critical tension for root water uptake (m) | Given in Tables 3 and 4 for the different crops. DEVELOPMENT DEFINITION. |
| ZALP | Correction factor for evaporation from wet canopy. | Given in Tables 3 and 4 for the different crops. DEVELOPMENT DEFINITION |
| ZDATEMIN | The day number corresponding to LAIMIN and ROOTINIT | Values given in Table 3, set one day after emergence for summer crops and as day 90 for the winter crops. The growth is expected to increase significantly after this date. DEVELOPMENT DEFINITION. |

### Irrigation

This is used as a way to apply the substance to the soil

| Parameter and description | Value, source & comments |
| --- | --- |
| AMIR | Amount of irrigation water applied (mm) in which the substance is mixed. | DEVELOPMENT DEFINITION 1000 l/ha = 1 m3/10,000 m2 = 0.1 mm is used |
| CONCI | Concentration of the substance in the irrigation water (mg m-3) | USER INPUT Calculated from the user-defined dose and AMIR |
| CRITDEF | Specification of criteria for irrigation | As there is no automatic irrigation, the value is set to (-1). DEVELOPMENT DEFINITION |
| IRRDAY | Day of irrigation (Day of substance application) | USER INPUT |
| IRREND | Time when the irrigation ends. | Given as hours and minutes as decimal fraction. Set to 9.2. DEVELOPMENT DEFINITION |
| IRRSTART | Time when the irrigation starts | Given as hours and minutes as decimal fraction. Set to 9. DEVELOPMENT DEFINITION |
| NIRR | Number of irrigations | USER INPUT |
| ZFINT | The fraction of the substance which is intercepted | FOCUS DEFINITION. ZFINT is set to zero. This solution is also recommended for the other models. Crop interception must be estimated manually, from the table in the FOCUS report, and subtracted from the specified dose. |

## Output specification

Output variables are selected to allow calculation of a water-and substance balance for a 1 m profile and for the full profile, as well as for calculating target quantities for EU registration purposes. Daily values of each variable are stored in the output .bin files.

### Miscellaneous (water)

| Parameter and description | Value, source & comments |
| --- | --- |
| WFLOWOUT | Water flow rate out of layer from macropores (mm hr-1) | Specified for layer 12, the output depth |
| WOUT | Water flow rate out of layer from micropores (mm hr-1) | Specified for layer 12, the output depth |

Water balance

| Parameter and description | Value, source & comments |
| --- | --- |
| CCET | Accumulated actual evapotranspiration (mm) |  |
| PRECIRA | Accumulated precipitation and irrigation (mm) |  |
| TRUNOFF | Accumulated surface runoff (mm) |  |
| TSTOREMI | Total water storage in micropores through the whole profile (mm) | The figure relates to the full profile and not the water balance at 1 m depth. |
| TSTOREMA | Total water storage in macropores through the whole profile (mm) | The figure relates to the full profile and not the water balance at 1 m depth. |
| TFLOWOUT | Total accumulated percolation (mm) (micropores and macropores) | The figure relates to the bottom of the profile, and not to the water balance at 1m depth. |

### Miscellaneous, other

| Parameter and description | Value, source & comments |
| --- | --- |
| DEGMAC | Solute degraded in soil macropores (mass m-2 h-1) | Only used as input for metabolite simulation |
| DEGMIC | Solute degraded in soil micropores (mass m-2 h-1) | Only used as input for metabolite simulation |
| SFLOW | Solute flow rate out of layer, micropores (mass m2 h-1) | For the result layer (12) only |
| SFLOWOUT | Solute flow rate out of layer, macropores (mass m2 h-1) | For the result layer (12) only |

### Solute balance

| Parameter and description | Value, source & comments |
| --- | --- |
| TADMA | Solute storage in profile, macropores only, solid phase (mass m-2) |  |
| TADMI | Solute storage in profile, micropores only, solid phase (mass m-2) |  |
| TDEG | Accumulated total degradation in the soil (mass m-2) | For this parameter, the value for the upper meter and for the profile is identical, due to the fact that degradation is specified for the upper meter only. |
| TUPT | Accumulated uptake of solute by crop, (mass m-2) | If the root depth is less than one meter, the value for the profile is identical to the value for the upper meter. |
| TCAM | Solute storage in macropores in the liquid phase, for the profile (mass m-2) |  |
| TPAM | Solute storage in micropores in the liquid phase for the profile (mass m-2) |  |
| TSOUT | Accumulated solute leaching (total for macro- and micropores) (mass m-2) |  |
| TSRUN | Accumulated amount of solute lost in runoff (mass m-2) |  |

## Run specification

The run specification should be daily outputs, with user start time given as 1901/01/01 and user specified end time, depending on the length of the simulation (26, 46 or 66 years).

Table 1  Soil hydraulic properties, Van Genuchten/Mualem parameters (restricted form, m=1-1/n)

| depth | qs | qr | a | n | Water content | Ksat | l | AW@ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| cm | m3 m-3 | m3 m-3 | m-1 | - | 10kPa m3 m-3 | 1600kPa m3 m-3 | m s-1 *10-6 | - | mm |
| 0-25 | 0.43 | 0.0 | 5.00 | 1.080 | 0.374 | 0.253 | 20.00 | 0.50 | 30.25 |
| 25-50 | 0.44 | 0.0 | 5.00 | 1.095 | 0.372 | 0.235 | 30.00 | 0.50 | 34.25 |
| 50-60 | 0.44 | 0.0 | 5.00 | 1.095 | 0.372 | 0.235 | 50.00 | 2.50 | 13.70 |
| 60-100 | 0.44 | 0.0 | 1.50 | 1.160 | 0.386 | 0.185 | 12.00 | -2.00 | 80.40 |
| 100-120 | 0.44 | 0.0 | 1.50 | 1.160 | 0.386 | 0.185 | 12.00 | -2.00 | - |
| 120-190 | 0.49 | 0.0 | 1.07 | 1.280 | 0.417 | 0.116 | 9.06 | -1.50 | - |
| 190-260 | 0.42 | 0.0 | 1.91 | 1.152 | 0.362 | 0.176 | 14.81 | -1.18 | - |

@ Plant available water in the soil layer.

Plant available water in the top 1 m is 158.6 mm.

Table 2  Soil hydraulic properties, Brooks-Corey/Mualem parameters (as used in the MACRO model)

| depth | qb | qr | hb | b | Water content | Kb | l | AW@ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| cm | m3 m-3 | m3 m-3 | m | - | 10kPa m3 m-3 | 1600kPa m3 m-3 | mm h-1 | - | mm |
| 0-25 | 0.41 | 0.0 | 0.2 | 0.07 | 0.366 | 0.258 | 0.25 | -0.50 | 27.00 |
| 25-50 | 0.43 | 0.0 | 0.2 | 0.09 | 0.372 | 0.237 | 0.50 | -0.50 | 33.75 |
| 50-60 | 0.43 | 0.0 | 0.2 | 0.09 | 0.372 | 0.237 | 1.00 | 1.50 | 13.50 |
| 60-100 | 0.43 | 0.0 | 0.4 | 0.14 | 0.378 | 0.188 | 1.00 | -4.00 | 76.00 |
| 100-120 | 0.43 | 0.0 | 0.4 | 0.14 | 0.378 | 0.188 | 1.00 | -4.00 | - |
| 120-190 | 0.47 | 0.0 | 0.3 | 0.19 | 0.374 | 0.150 | 3.25 | -3.50 | - |
| 190-260 | 0.40 | 0.0 | 0.3 | 0.14 | 0.338 | 0.176 | 1.00 | -3.50 | - |

Note: Ksat and qs are the same as for the Mualem/van Genuchten fit shown in Table B.1.

@ Plant available water in the soil layer.

Plant available water in the top 1 m is 150.3 mm.

Table 3  MACRO parameters for the annual crops for Chateaudun.

|  | Crop |
| --- | --- |
| Parameter | apples | vines | potatoes | sugar beet | cabbage | carrots | maize | onion | peas | spring cereals | tomatoes | winter cereals | oil seed rape (w) |
| Crop | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |
| Chapar |  |  |  |  | on | on |  |  |  |  |  |  |  |
| Date |  |  |  |  | 197 | 180 |  |  |  |  |  |  |  |
| Beta | 0.2 | 0.2 | 0.5 | 0.2 | 0.5 | 0.5 | 0.2 | 0.5 | 0.5 | 0.2 | 0.5 | 0.1 | 0.1 |
| Cancap | 4 | 3 | 2 | 2.5 | 2 | 2 | 3 | 2 | 2 | 2 | 2 | 3 | 3 |
| Cform | 1.5 | 1.5 | 1.7 | 1.7 | 1.5 | 1.5 | 1.7 | 1.5 | 1.7 | 2 | 1.3 | 2 | 2 |
| Critair | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 |
| Dform | 0.7 | 0.7 | 0.3 | 1 | 1 | 1 | 0.3 | 1 | 0.3 | 0.3 | 0.3 | 0.2 | 0.2 |
| IDMax | 151 | 212 | 166 | 196 | 151/248 | 110/222 | 227 | 181 | 158 | 161 | 181 | 151 | 110 |
| IDStart | 91 | 91 | 120 | 106 | 110/212 | 69/191 | 121 | 115 | 95 | 69 | 130 | 299 | 250 |
| Iharv | 274 | 305 | 244 | 288 | 196/288 | 151/263 | 274 | 244 | 227 | 201 | 237 | 196 | 191 |
| Laihar | 0.01 | 0.01 | 2 | 5 | 3 | 3 | 2 | 3 | 3 | 2 | 3 | 2 | 2 |
| Laimax | 4 | 6 | 4 | 5 | 3 | 3 | 4.5 | 3 | 4 | 5 | 6 | 7.5 | 4 |
| Laimin | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.3 | 1 | 1 |
| Rootinit | 1.89 | 1.89 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.01 | 0.1 | 0.2 | 0.2 |
| Rootmax | 1.9 | 1.9 | 0.6 | 1 | 0.6 | 0.8 | 0.8 | 0.6 | 0.6 | 0.6 | 0.8 | 0.8 | 1 |
| Rpin | 60 | 60 | 75 | 67 | 75 | 75 | 67 | 75 | 67 | 60 | 67 | 60 | 60 |
| Waten | 20 | 20 | 10 | 20 | 10 | 10 | 20 | 10 | 10 | 20 | 10 | 50 | 50 |
| Zalp | 3 | 2 | 1 | 1 | 1 | 1 | 1.5 | 1 | 1 | 1 | 1 | 1 | 1 |
| Zdatemin | 92 | 92 | 121 | 107 | 111/213 | 70/192 | 122 | 116 | 96 | 70 | 131 | 90 | 90 |

Table 4  MACRO crop parameters for grass/alfalfa

| Parameter | Value |
| --- | --- |
| Crop | 3 |
| Chapar | OFF |
| Beta | 0.2 |
| Cancap | 2 |
| Critair | 5 |
| Laic | 5 |
| Rootdep | 0.5 |
| Rpin | 67 |
| Waten | 20 |
| Zalp | 1 |
| Hcrop | 0.2 |

Table 5 Solute-related parameters : fixed for all substances in FOCUS

| Parameter | Value |
| --- | --- |
| Aexc | 0 |
| Conc | 0 |
| Dv | 5 |
| Zmix | 1 |
| Candeg | 0.2 |
| Fext | 0 |
| Fracmac | 0.02 |
| Zfint | 0 |

Table 6 User-defined properties : dummy substances A, B, C and its metabolite, and D

|  | Substance |
| --- | --- |
| Parameter | A | B | C | metabolite | D |
| Diff | 5.00E-10 | 5.00E-10 | 5.00E-10 | 5.00E-10 | 5.00E-10 |
| Fstar | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 |
| aDegmal(1-4) | 0.0125 | 0.0375 | 0.0375 | 0.00750 | 0.0375 |
| aDegmal(5-8) | 0.00639 | 0.01918 | 0.01918 | 0.00385 | 0.01918 |
| aDegmal(9-12) | 0.00379 | 0.01137 | 0.01137 | 0.00228 | 0.01137 |
| aDegmal(13-15) | 0 | 0 | 0 | 0 | 0 |
| Expb | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 |
| Fconvert |  |  |  | 0.53 |  |
| Freund | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 |
| Tref | 20 | 20 | 20 | 20 | 20 |
| Tresp | 0.079 | 0.079 | 0.079 | 0.079 | 0.079 |
| Zkd(1-4) | 1.41 | 0.233 | 2.36 | 0.712 | 0.82 |
| Zkd(5-7) | 0.95 | 0.156 | 1.58 | 0.478 | 0.551 |
| Zkd(8) | 0.72 | 0.119 | 1.2 | 0.364 | 0.418 |
| Zkd(9-13) | 0.31 | 0.051 | 0.516 | 0.156 | 0.18 |
| Zkd(14-15) | 0.28 | 0.046 | 0.464 | 0.14 | 0.162 |
| bAmir | 0.1 | 0.1 | 0.1 | 0 | 0.1 |
| bConci | 1E6 | 1E6 | 1E6 | 0 | 1E6 |

a Degmas, Degmil, and Degmis receive the same values

b dose applied on day 69 (irrday) between 6 (Irrstart) and 6.5 (Irrend)

## References

Jarvis N, 1994. The MACRO Model (Version 3.1). Technical Description and Sample Simulations. Department of Soil Sciences, Swedish University of Agricultural Sciences. Reports and Dissertations, 19. Uppsala 1994.