APPENDIX D

parameterisation of runoff INPUT

The PRZM model has been parameterized to calculate surface runoff and erosion inputs for the runoff scenarios R1 to R4.  Table D.1 lists general cropping parameters that apply to all four scenarios while Tables D.2 to D.17 list scenario-specific parameters.  Descriptions of the individual parameters are provided in the PRZM User Manual in Appendix K.

## Crop parameters

## Table D.1. General cropping parameters for all runoff scenarios for PRZM

|  | Pan evap factor, PFAC | Canopy interceptn,CINTCP | Maximum coverage, COVMAX | Maximum height, HTMAX | USLEC factor, fallow | USLEC factor, cropping | USLEC factor, residue |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Cereals, Spring | 0.92 | 0.15 | 90 | 110 | 0.9 | 0.2 | 0.4 |
| Cereals, Winter | 0.84 | 0.15 | 90 | 100 | 0.9 | 0.2 | 0.4 |
| Citrus | 0.69 | 0.30 | 70 | 250 | 0.2 | 0.2 | 0.2 |
| Field beans | 0.89 | 0.15 | 80 | 150 | 0.9 | 0.2 | 0.4 |
| Grass/alfalfa | 1.00 | 0.15 | 90 | 40 | 0.02 | 0.02 | 0.02 |
| Hops | 0.72 | 0.30 | 90 | 250 | 0.9 | 0.2 | 0.4 |
| Legumes | 0.96 | 0.15 | 85 | 100 | 0.9 | 0.2 | 0.4 |
| Maize | 0.94 | 0.30 | 90 | 250 | 0.9 | 0.2 | 0.4 |
| Oilseed rape, spring | 0.93 | 0.15 | 90 | 140 | 0.9 | 0.2 | 0.4 |
| Oilseed rape, winter | 0.78 | 0.15 | 90 | 140 | 0.9 | 0.2 | 0.4 |
| Olive | 0.83 | 0.30 | 80 | 250 | 0.2 | 0.2 | 0.2 |
| Pome/stone fruit | 0.83 | 0.30 | 80 | 250 | 0.9 | 0.2 | 0.4 |
| Potatoes | 0.94 | 0.15 | 80 | 100 | 0.9 | 0.2 | 0.4 |
| Soybean | 0.92 | 0.25 | 85 | 170 | 0.9 | 0.2 | 0.4 |
| Sugar beets | 0.93 | 0.15 | 90 | 40 | 0.9 | 0.2 | 0.4 |
| Sunflower | 0.86 | 0.30 | 90 | 150 | 0.9 | 0.2 | 0.4 |
| Tobacco | 0.98 | 0.25 | 90 | 250 | 0.9 | 0.2 | 0.4 |
| Vegetables, bulb | 0.91 | 0.15 | 60 | 60 | 0.9 | 0.2 | 0.4 |
| Vegetables, fruiting | 0.97 | 0.15 | 80 | 110 | 0.9 | 0.2 | 0.4 |
| Vegetables, leafy | 0.97 | 0.15 | 90 | 30 | 0.9 | 0.2 | 0.4 |
| Vegetables, root | 0.96 | 0.15 | 80 | 40 | 0.9 | 0.2 | 0.4 |
| Vines | 0.72 | 0.30 | 85 | 170 | 0.2 | 0.2 | 0.2 |

## Table D.2.  R1 scenario-specific parameters for PRZM

| Evaporation depth during fallow period (ANETD) | 15 cm |
| --- | --- |
| Bottom boundary temperature (BBT) | 10.0 oC |
| Selected meteorological years First application March to May First application June to September First application October to February | 1984 1978 1978 |

## Table D.3.  R1 scenario-specific cropping parameters for PRZM

| Crop group | Maximum rooting depth, AMXDR (cm) | Emergence date | Maturation date | Harvest date | Fallow date |
| --- | --- | --- | --- | --- | --- |
| Cereals, winter | 130 | 12/11 | 10/6 | 31/7 | 1/11 |
| Field beans | 90 | 10/4 | 10/7 | 25/8 | 1/11 |
| Hops b | 100 | 15/4 | 27/8 | 1/9 | 1/11 |
| Legumes | 80 | 15/4 | 12/6 | 15/8 | 1/11 |
| Maize | 130 | 3/5 | 7/8 | 25/9 | 1/11 |
| Oil seed rape, spring | 100 | 10/4 | 7/6 | 15/8 | 1/11 |
| Oil seed rape, winter | 120 | 4/9 | 25/5 | 10/7 | 1/11 |
| Pome/stone fruit b | 150 | 15/4 | 1/7 | 30/10 | 1/11 |
| Potatoes | 70 | 5/5 | 25/6 | 8/9 | 1/11 |
| Sugar beets | 120 | 16/4 | 15/7 | 10/10 | 1/11 |
| Sunflowers | 100 | 1/5 | 5/7 | 31/8 | 1/11 |
| Vegetables, bulb | 40 | 20/4 | 25/6 | 25/8 | 1/11 |
| Vegetables, leafy a | 60 | 20/4 31/7 | 31/5 5/9 | 15/7 15/10 | 20/7 1/11 |
| Vegetables, root | 40 | 20/4 | 25/6 | 10/8 | 1/11 |
| Vines b | 100 | 15/4 | 1/7 | 30/10 | 1/11 |

a 2 crops per season with simulations performed separately for early crop and late crop

b Perennial crops

## Table D.4.  R1 scenario-specific runoff curve numbers and met files for PRZM

| Crop group | Runoff curve number (antecedent moisture condition II) | PRZM met file |
| --- | --- | --- |
|  | Emergence (cropping) | Maturation (cropping) | Harvest (residue) | Fallow |  |
| Cereals, winter | 81 | 81 | 86 | 91 | R1noirr |
| Field beans | 82 | 82 | 87 | 91 | R1noirr |
| Hops b | 70 | 70 | 70 | 70 | R1hopsc |
| Legumes | 78 | 78 | 85 | 91 | R1legum |
| Maize | 82 | 82 | 87 | 91 | R1maize |
| Oil seed rape, spring | 81 | 81 | 86 | 91 | R1noirr |
| Oil seed rape, winter | 81 | 81 | 86 | 91 | R1noirr |
| Pome/stone fruit b | 70 | 70 | 70 | 70 | R1noirr |
| Potatoes | 82 | 82 | 87 | 91 | R1potat |
| Sugar beets | 82 | 82 | 87 | 91 | R1sugbt |
| Sunflowers | 82 | 82 | 87 | 91 | R1sunfl |
| Vegetables, bulb | 82 | 82 | 87 | 91 | R1buveg |
| Vegetables, leafy a | 82 | 82 | 87 | 91 | R1leveg |
| Vegetables, root | 82 | 82 | 87 | 91 | R1roveg |
| Vines b | 70 | 70 | 70 | 70 | R1noirr |

a 2 crops per season with simulations performed separately for early crop and late crop

b Perennial crops

c 70th percentile met year selected, appropriate for hops in scenario R1

## Table D.5.  R2 scenario-specific parameters for PRZM

| Evaporation depth during fallow period (ANETD) | 25 cm |
| --- | --- |
| Bottom boundary temperature (BBT) | 14.8 oC |
| Selected meteorological years First application March to May First application June to September First application October to February | 1977 1989 1977 |

## Table D.6.  R2 scenario-specific crop input parameters for PRZM

| Crop group | Maximum rooting depth, AMXDR (cm) | Emergence date | Maturation date | Harvest date | Fallow date |
| --- | --- | --- | --- | --- | --- |
| Field beans | 60 | 10/3 | 15/5 | 31/8 | 1/11 |
| Grass / alfalfa b | 50 | 2/1 | 3/1 | 30/12 | 31/12 |
| Legumes | 50 | 20/4 | 20/5 | 25/6 | 1/11 |
| Maize | 80 | 1/5 | 15/8 | 1/10 | 1/11 |
| Pome/stone fruit b | 150 | 15/3 | 31/7 | 30/9 | 1/11 |
| Potatoes | 70 | 15/3 | 30/5 | 15/6 | 1/11 |
| Vegetables, bulb | 60 | 28/2 | 15/5 | 31/5 | 1/11 |
| Vegetables, fruiting | 60 | 15/3 | 15/6 | 31/8 | 1/11 |
| Vegetables, leafya | 60 | 28/2 31/7 | 15/5 31/8 | 1/7 15/11 | 15/7 1/12 |
| Vegetables, roota | 60 | 28/2 22/7 | 1/5 15/9 | 31/5 15/10 | 1/7 1/11 |
| Vines b | 150 | 15/3 | 31/7 | 30/9 | 1/11 |

a 2 crops per season with simulations performed separately for early crop and late crop

b Perennial crops

## Table D.7.  R2 scenario-specific runoff curve numbers and met files for PRZM

| Crop group | Runoff curve number (antecedent moisture condition II) | PRZM met file |
| --- | --- | --- |
|  | Emergence (cropping) | Maturation (cropping) | Harvest (residue) | Fallow |  |
| Field beans | 78 | 78 | 83 | 88 | R2noirr |
| Grass / alfalfa b | 63 | 63 | 63 | 63 | R2noirr |
| Legumes | 74 | 74 | 81 | 88 | R2noirr |
| Maize | 78 | 78 | 83 | 88 | R2noirr |
| Pome/stone fruit b | 63 | 63 | 63 | 63 | R2noirr |
| Potatoes | 78 | 78 | 83 | 88 | R2noirr |
| Vegetables, bulb | 78 | 78 | 83 | 88 | R2noirr |
| Vegetables, fruiting | 78 | 78 | 83 | 88 | R2noirr |
| Vegetables, leafy a | 78 | 78 | 83 | 88 | R2noirr |
| Vegetables, root a | 78 | 78 | 83 | 88 | R2noirr |
| Vines b | 63 | 63 | 63 | 63 | R2noirr |

a 2 crops per season with simulations performed separately for early crop and late crop

b Perennial crops

## Table D.8.  R3 scenario-specific parameters for PRZM

| Evaporation depth during fallow period (ANETD) | 25 cm |
| --- | --- |
| Bottom boundary temperature (BBT) | 13.5 oC |
| Selected meteorological years First application March to May First application June to September First application October to February | 1980 1975 1980 |

## Table D.9. R3 scenario-specific cropping parameters for PRZM

| Crop group | Maximum rooting depth, AMXDR (cm) | Emergence date | Maturation date | Harvest date | Fallow date |
| --- | --- | --- | --- | --- | --- |
| Cereals, winter | 120 | 1/12 | 10/5 | 1/7 | 1/11 |
| Field beans | 60 | 2/4 | 1/5 | 15/6 | 1/11 |
| Grass / alfalfa b | 50 | 2/1 | 3/1 | 30/12 | 31/12 |
| Legumes | 50 | 21/4 | 20/5 | 25/6 | 1/11 |
| Maize | 120 | 1/5 | 25/7 | 1/10 | 1/11 |
| Oil seed rape, winter | 80 | 5/10 | 20/4 | 5/6 | 1/11 |
| Pome/stone fruit b | 150 | 1/4 | 31/5 | 15/10 | 1/11 |
| Potatoes | 60 | 10/4 | 30/5 | 1/9 | 1/11 |
| Soybean | 60 | 10/5 | 31/7 | 5/10 | 1/11 |
| Sugar beets | 70 | 20/3 | 25/6 | 3/9 | 1/11 |
| Sunflowers | 140 | 15/4 | 25/6 | 20/9 | 1/11 |
| Tobacco | 100 | 20/5 | 20/7 | 5/10 | 1/11 |
| Vegetables, bulb | 40 | 1/3 | 15/5 | 31/5 | 1/11 |
| Vegetables, fruiting | 100 | 10/5 | 30/6 | 25/8 | 1/11 |
| Vegetables, leafy a | 60 | 1/3 15/6 | 1/5 15/8 | 1/6 15/9 | 10/6 1/11 |
| Vegetables, root | 40 | 26/2 | 15/4 | 13/5 | 1/11 |
| Vines b | 150 | 1/4 | 31/7 | 1/11 | 1/11 |

a 2 crops per season with simulations performed separately for early crop and late crop

b Perennial crops

## Table D.10.  R3 scenario-specific runoff curve numbers for PRZM

| Crop group | Runoff curve number (antecedent moisture condition II) | PRZM met file |
| --- | --- | --- |
|  | Emergence (cropping) | Maturation (cropping) | Harvest (residue) | Fallow |  |
| Cereals, winter | 81 | 81 | 86 | 91 | R3noirr |
| Field beans | 82 | 82 | 87 | 91 | R3fldbn |
| Grass / alfalfa b | 70 | 70 | 70 | 70 | R3noirr |
| Legumes | 78 | 78 | 85 | 91 | R3legum |
| Maize | 82 | 82 | 87 | 91 | R3maize |
| Oil seed rape, winter | 81 | 81 | 86 | 91 | R3noirr |
| Pome/stone fruit b | 70 | 70 | 70 | 70 | R3noirr |
| Potatoes | 82 | 82 | 87 | 91 | R3potat |
| Soybean | 82 | 82 | 87 | 91 | R3soybn |
| Sugar beets | 82 | 82 | 87 | 91 | R3sugbt |
| Sunflowers | 82 | 82 | 87 | 91 | R3sunfl |
| Tobacco | 82 | 82 | 87 | 91 | R3tobac |
| Vegetables, bulb | 82 | 82 | 87 | 91 | R1buveg |
| Vegetables, fruiting | 82 | 82 | 87 | 91 | R3frveg |
| Vegetables, leafy a | 82 | 82 | 87 | 91 | R3leveg |
| Vegetables, root | 82 | 82 | 87 | 91 | R3roveg |
| Vines b | 70 | 70 | 70 | 70 | R3noirr |

a 2 crops per season with simulations performed separately for early crop and late crop

b Perennial crops

Table D.11.  R4 scenario-specific parameters for PRZM

| Evaporation depth during fallow period (ANETD) | 25 cm |
| --- | --- |
| Bottom boundary temperature (BBT) | 14.0 oC |
| Selected meteorological years First application March to May First application June to September First application October to February | 1984 1985 1979 |

Table D.12.  R4 scenario-specific cropping parameters for PRZM

| Crop group | Maximum rooting depth, AMXDR (cm) | Emergence date | Maturation date | Harvest date | Fallow date |
| --- | --- | --- | --- | --- | --- |
| Cereals, spring | 120 | 15/3 | 15/5 | 20/7 | 1/11 |
| Cereals, winter | 120 | 10/11 | 15/5 | 15/7 | 1/11 |
| Citrus b | 150 | 2/1 | 3/1 | 30/12 | 31/12 |
| Field beans | 60 | 2/4 | 1/5 | 15/6 | 1/11 |
| Legumes | 50 | 21/4 | 20/5 | 25/6 | 1/11 |
| Maize | 100 | 10/4 | 15/6 | 31/8 | 1/11 |
| Olives b | 150 | 2/1 | 3/1 | 30/12 | 31/12 |
| Pome/stone fruit b | 150 | 15/3 | 31/5 | 15/10 | 1/11 |
| Soybean | 60 | 10/3 | 20/7 | 20/9 | 1/11 |
| Sunflowers | 100 | 30/3 | 20/6 | 20/8 | 1/11 |
| Vegetables, bulb | 40 | 1/3 | 15/5 | 31/5 | 1/11 |
| Vegetables, fruiting | 80 | 20/4 | 10/6 | 15/7 | 1/11 |
| Vegetables, leafy a | 60 | 1/3 15/6 | 1/5 15/8 | 1/6 15/9 | 10/6 1/11 |
| Vegetables, root | 40 | 26/2 | 15/4 | 13/5 | 1/11 |
| Vines b | 150 | 10/3 | 20/7 | 20/9 | 1/11 |

a 2 crops per season with simulations performed separately for early crop and late crop

b Perennial crops

## Table D.13.  R4 scenario-specific runoff curve numbers for PRZM

| Crop group | Runoff curve number (antecedent moisture condition II) | PRZM met file |
| --- | --- | --- |
|  | Emergence (cropping) | Maturation (cropping) | Harvest (residue) | Fallow |  |
| Cereals, spring | 81 | 81 | 86 | 91 | R4noirr |
| Cereals, winter | 81 | 81 | 86 | 91 | R4noirr |
| Citrus b | 70 | 70 | 70 | 70 | R4citrs |
| Field beans | 82 | 82 | 87 | 91 | R4fldbn |
| Legumes | 78 | 78 | 85 | 91 | R4legum |
| Maize | 82 | 82 | 87 | 91 | R4maize |
| Olives b | 70 | 70 | 70 | 70 | R4noirr |
| Pome/stone fruit b | 70 | 70 | 70 | 70 | R4noirr |
| Soybean | 82 | 82 | 87 | 91 | R4soybn |
| Sunflowers | 82 | 82 | 87 | 91 | R4sunfl |
| Vegetables, bulb | 82 | 82 | 87 | 91 | R4buveg |
| Vegetables, fruiting | 82 | 82 | 87 | 91 | R4frveg |
| Vegetables, leafy a | 82 | 82 | 87 | 91 | R4leveg |
| Vegetables, root | 82 | 82 | 87 | 91 | R4roveg |
| Vines b | 70 | 70 | 70 | 70 | R4noirr |

a 2 crops per season with simulations performed separately for early crop and late crop

b Perennial crops

Soil and site parameters

All basic properties are derived from measured data for the local soil type, unless otherwise indicated by notation in the tables. For other PRZM parameters, the method of parameter estimation is indicated by the notations in the tables.

Table D.14.  R1 soil and site parameters for PRZM

| Horizon (FAO, 1990) | Ap | Bw | BC |
| --- | --- | --- | --- |
| Depth (cm) | 0-30 | 30-60 | 60-100+ |
| BASIC PROPERTIES |  |  |  |
| Sand (%) | 5 | 6 | 5 |
| Silt (%) | 82 | 83 | 84 |
| Clay (%) | 13 | 11 | 11 |
| Texture (FAO, 1990; USDA, 1999) | silt loam | silt loam | silt loam |
| Organic carbon (%) | 1.2 | 0.3 | 0.1 |
| Bulk density (g/cm3) | 1.35 | 1.45 | 1.48 a |
| PH | 7.3 | 7.6 | 8.0 |
| Structure (FAO, 1990) |  |  |  |
| Development | Weak | Weak | Very weak |
| Size | Fine | Medium | Very coarse |
| Shape | Subangular blocky | Subangular blocky | Subangular blocky |
| HYDRAULIC PROPERTIES |  |  |  |
| Field capacity (% volume) | 33.8 b | 28.6 b | 27.7 b |
| Wilting point (% volume) | 14.1 b | 11.1 b | 10.8 b |
| RUNOFF & SOIL LOSS PROPERTIES |  |  |  |
| Parameter | Value | Selection criteria | Reference |
| Hydrologic group (HGRP) | C | appropriate for soil type | FOCUS definition |
| USLE K factor (USLEK) | 0.42 | silt/silt loam, 2% OM | PRZM manual |
| USLE LS factor (USLELS) | 0.33 | 45 m length, 3% slope | PRZM manual |
| USLE P factor (USLEP) | 0.50 | contouring, 3% slope | PRZM manual |
| Area of field (AFIELD) | 0.45 ha | assumption for scenario | FOCUS definition |
| IREG | 3 | even monthly rain distrib. | FOCUS definition |
| Slope (SLP) | 3% | appropriate for scenario | FOCUS definition |
| HL | 20 m | assumption for scenario | FOCUS definition |
| Manning’s coefficient | 0.10 | fallow, no-till or coulter | PRZM manual |

a 	Estimated value using SSLRC algorithms and measured local data for the soil type.

b 	Calculated using PRZM pedo-transfer functions with other data given in the table

(FC = –33 kPa; WP = –1500 kPa).

Table D.15.  R2 soil and site parameters for PRZM

| Horizon (FAO, 1990) | Ap | Ah | AB1 | AB2 |
| --- | --- | --- | --- | --- |
| Depth (cm) | 0-20 | 20-45 | 45-65 | 65-100 |
| BASIC PROPERTIES |  |  |  |  |
| Sand (%) | 67 | 72 | 75 | 74 |
| Silt (%) | 19 | 16 | 13 | 16 |
| Clay (%) | 14 | 12 | 12 | 10 |
| Texture (FAO, 1990; USDA, 1999) | sandy loam | sandy loam | sandy loam | sandy loam |
| Organic carbon (%) | 4.0 | 2.4 | 0.8 | 0.5 a |
| Bulk density (g/cm3) | 1.15 b | 1.29 b | 1.36 b | 1.41 b |
| pH | 4.5 | 4.9 | 5.4 | 5.3 |
| Structure (FAO, 1990) |  |  |  |  |
| Development | Moderate | Weak | Weak | Weak |
| Size | Medium | Medium | Medium | Medium |
| Shape | Subangular blocky | Subangular blocky | Subangular blocky | Subangular blocky |
| HYDRAULIC PROPERTIES |  |  |  |  |
| Field capacity (% volume) | 36 c | 27 c | 19 c | 17 c |
| Wilting point (% volume) | 18 c | 14 c | 10 c | 8 c |
| RUNOFF & SOIL LOSS PROPERTIES |  |  |  |  |
| Parameter | Value | Selection criteria | Reference |
| Hydrologic group (HGRP) | B / C | appropriate for soil type | FOCUS definition |
| USLE K factor (USLEK) | 0.19 | sandy loam, 4% OM | PRZM manual |
| USLE LS factor (USLELS) | 0.66 | 45 m length, 5% slope | PRZM manual |
| USLE P factor (USLEP) | 0.50 | contouring, 5% slope | PRZM manual |
| Area of field (AFIELD) | 0.45 ha | assumption for scenario | FOCUS definition |
| IREG | 2 | heavier winter rain | FOCUS definition |
| Slope (SLP) | 5% | 20% slope, terraced to 5% | FOCUS definition |
| HL | 20 m | assumption for scenario | FOCUS definition |
| Manning’s coefficient | 0.10 | fallow, no-till or coulter | PRZM manual |

a 	Estimated value based on horizon type and value for horizon above.

b 	Estimated value using SSLRC algorithms and measured local data for the soil type.

c 	Calculated using PRZM pedo-transfer functions with other data given in the table

(FC = –33 kPa; WP = –1500 kPa).

Table D.16.  R3 soil and site parameters for PRZM

| Horizon (FAO, 1990) | Ap1 | Ap2 | Bk | C |
| --- | --- | --- | --- | --- |
| Depth (cm) | 0 – 45 | 45 - 75 | 75 – 145 | 145 – 160 |
| BASIC PROPERTIES |  |  |  |  |
| Sand (%) | 23 | 25 | 17 | 14 |
| Silt (%) | 43 | 42 | 48 | 50 |
| Clay (%) | 34 | 33 | 35 | 36 |
| Texture (FAO, 1990; USDA, 1999) | clay loam | clay loam | silty clay loam | silty clay loam |
| Organic carbon (%) | 1.0 | 1.0 | 0.35 | 0.29 |
| Bulk density (g/cm3) | 1.46a | 1.49 a | 1.52 a | 1.54 a |
| pH | 7.9 | 7.9 | 8.3 | 8.6 |
| Structure (FAO, 1990) |  |  |  |  |
| Development | Moderate | Moderate | Weak | Weak |
| Size | fine | Fine | coarse | Very coarse |
| Shape | Granular | granular | Subangular blocky | Angular blocky |
| HYDRAULIC PROPERTIES |  |  |  |  |
| Field capacity (% volume) | 37 b | 35 b | 36 b | 36 b |
| Wilting point (% volume) | 22 b | 21 b | 21 b | 22 b |
| RUNOFF & SOIL LOSS PROPERTIES |  |  |  |  |
| Parameter | Value | Selection criteria | Reference |
| Hydrological group (HGRP) | C | appropriate for soil type | FOCUS definition |
| USLE K factor (USLEK) | 0.25 | clay loam, 1% OM | PRZM manual |
| USLE LS factor (USLELS) | 0.66 | 45 m length, 5% slope | PRZM manual |
| USLE P factor (USLEP) | 0.50 | contouring, 5% slope | PRZM manual |
| Area of field (AFIELD) | 0.45 ha | assumption for scenario | FOCUS definition |
| IREG | 3 | even seasonal rain | FOCUS definition |
| Slope (SLP) | 5% | 10% slope, terraced to 5% | FOCUS definition |
| HL | 20 m | assumption for scenario | FOCUS definition |
| Manning’s coefficient | 0.10 | fallow, no-till or coulter | PRZM manual |

a 	Estimated using SSLRC pedo-transfer functions with other data given in the table and checked against data in the PRZM manual.

b 	Calculated using PRZM pedo-transfer functions with other data given in the table

(FC = –33 kPa; WP = –1500 kPa).

Table D.17.  R4 soil and site parameters for PRZM

| Horizon (FAO, 1990) | Ap1 | Ap2 | 2C1 | 2C2 |
| --- | --- | --- | --- | --- |
| Depth (cm) | 0-30 | 30-60 | 60 - 170 | 170-300 |
| BASIC PROPERTIES |  |  |  |  |
| Sand (%) | 53 | 53 | 69 | 65 |
| Silt (%) | 22 | 22 | 24 | 27 |
| Clay (%) | 25 | 25 | 7 | 8 |
| Texture (FAO, 1990; USDA, 1999) | sandy clay loam | sandy clay loam | sandy loam | sandy loam |
| Organic carbon (%) | 0.6 | 0.6 a | 0.08 | 0.08 |
| Bulk density (g/cm3) | 1.52 | 1.50 a | 1.49 | 1.50 |
| pH | 8.4 | 8.4 a | 8.8 | 8.8 |
| Structure (FAO, 1990) |  |  |  |  |
| Development | Moderate | Moderate | Apedal | Apedal |
| Size | Fine | Fine | N/A | N/A |
| Shape | Subangular blocky | Subangular blocky | Single grain | Single grain |
| HYDRAULIC PROPERTIES |  |  |  |  |
| Field capacity (% volume) | 26 b | 27 b | 14.5 b | 16 b |
| Wilting point (%volume) | 16 b | 16 b | 6 b | 7 b |
| RUNOFF & SOIL LOSS PROPERTIES |  |  |  |  |
| Parameter | Value | Selection criteria | Reference |
| Hydrologic group (HGRP) | C | appropriate for soil type | FOCUS definition |
| USLE K factor(USLEK) | 0.26 | sandy clay loam, 0.6% OM | PRZM manual |
| USLE LS factor (USLELS) | 0.66 | 45 m length, 5% slope | PRZM manual |
| USLE P factor (USLEP) | 0.50 | contouring, 5% slope | PRZM manual |
| Area of field (AFIELD) | 0.45 ha | assumption for scenario | FOCUS definition |
| IREG | 2 | heavier winter rain | FOCUS definition |
| Slope (SLP) | 5% | appropriate for scenario | FOCUS definition |
| HL | 20 m | assumption for scenario | FOCUS definition |
| Manning’s coefficient | 0.10 | fallow, no-till or coulter | PRZM manual |

a 	Estimated value based on horizon type and value for horizon above.

b 	Calculated using PRZM pedo-transfer functions with other data given in the table

(FC = –33 kPa; WP = –1500 kPa).