Version: 1.0

Date: October 1st, 2001

PELMO - Parameterisation for the FOCUS Groundwater Scenarios

About this document

The report on which this document is based is that of the FOCUS Groundwater Scenarios workgroup, which is an official guidance document in the context of 91/414/EEC [full citation is FOCUS (2000) “FOCUS groundwater scenarios in the EU review of active substances” Report of the FOCUS Groundwater Scenarios Workgroup, EC Document Reference SANCO/321/2000 rev.2, 202pp].  This document does not replace the official FOCUS report.  However, a need was identified to maintain the parameterisation of the models for the FOCUS groundwater scenarios in an up-to-date version controlled document, as changes become necessary.  That is the purpose of this document.

Summary of changes made since the official FOCUS Groundwater Scenarios Report (SANCO/321/2000 rev.2).

New in Version 1.0

Compared to the original report changes has been made in

- Figure C.4  Running PELMO simulations using WPELMO.EXE

- Parameterisation description, section on “soil scenario files”

- Parameterisation description, section on “substance files”

The changes were necessary to keep the parameterisation document up-to-date with the current model version.

The only other changes in this version compared with the original report are editorial ones.

## Summary

PELMO is a one dimensional simulation model simulating the vertical movement of chemicals in soil by chromatographic leaching. The first version of PELMO was released in 1991 (Klein, 1991). PELMO is based on the US-EPA’s PRZM 1 model  (Carsel et al, 1984), but was improved with regard to the requirements of the German authorities.  In version 2.01 of PELMO (released in 1995) the runoff routines were upgraded and routines for estimating the volatilisation of substances were added. PELMO 2.01 was validated within a joint project of the "Industrieverband Agrar" (IVA), the German Environmental Protection Agency and the "Fraunhofer-Institut für Umweltchemie und Ökotoxikologie" in Schmallenberg shared by the KfA Jülich and the SLFA Neustadt (Klein et al, 1997). In 1998 a complementary tool was added to PELMO 2.01 in order to enable the transformation of the applied a.i. to metabolites and to allow for further metabolism including the formation of CO2 (PELMO 3.0; Jene, 1998).  Recently, additional validation tests in lysimeters and field plots have been performed (Fent et al, 1998).

The PELMO version that was used for the implementation of the FOCUS-scenarios was developed in 1999 (PELMO 3.2). It was necessary to change the format of the scenario data files and the handling of leap years slightly because of the needs of the FOCUS-scenarios. Minor changes were also made in the routine that is estimating soil temperatures based on air temperatures to make sure that the results are correct also for soil depths below 1.0 m. Finally, the runoff routine in PELMO was calibrated based on field experiments by introducing a new parameter in the model (“fraction of soil water available for runoff”).

Table 1.1  Summary of the processes in PELMO

| Process | Approach |
| --- | --- |
| water movement | capacity-based water flow (tipping bucket approach) using a daily time step for all hydrological processes |
| substance movement | convection dispersion equation based on a daily time step |
| crop simulation | changing root zone during growing season, changing foliage (areal extent) during growing season, crop interception of water*, crop interception of substances*, foliar washoff*, foliar degradation* |
| degradation in soil | first order degradation rate, correction of rate constant with depth, soil moisture and soil temperatures |
| substance sorption to soil | Kd, Koc, Freundlich equation for sorption option for increase of sorption with time option for automated pH-dependence* |
| substance volatilisation (from soil) | simple model using Fick’s and Henry’s law |
| runoff | Soil Conservation Service curve number technique |
| drainage & preferential flow | not simulated |
| soil erosion* | Modified Universal Soil Loss Equation |
| soil temperature | An empirical model that uses air temperatures |
| plant uptake | simple model based on soil concentrations |
| substance applications | applications may be foliar sprays, applied to the soil surface, or incorporated into the soil; for soil incorporated applications a variety of soil distributions can be specified |
| metabolism | a sophisticated scheme with up to 8 metabolites (A -> B as well as A -> B -> C) may be simulated simultaneously with the parent |

* = turned off for the FOCUS scenarios

## Introduction

The PELMO version that was used for the implementation of the FOCUS-scenarios was developed in 1999 (PELMO 3.2). It was necessary to change the format of the scenario and pesticide data files and the handling of leap years slightly because of the needs of the FOCUS-scenarios. Minor changes were also made in the routine that is estimating soil temperatures based on air temperatures to make sure that the results are correct also for soil depths below 1.0 m. Finally, the runoff routine in PELMO was calibrated based on field experiments by introducing a new

parameter in the model (“fraction of soil water available for runoff”).

## Description of the PELMO shell

PELMO.EXE runs under Microsoft DOS. However, to make editing and creating of PELMO input files easier in a Microsoft Windows environment, a shell called WPELMO.EXE was built around PELMO.EXE.

### File handling

The information necessary to run PELMO.EXE is divided in a number of input data files. The shell WPELMO.EXE allows creating or editing of these files by the user. For each simulation a single substance data file (extension: PSM), a single scenario data file (extension: SZE) and a number of climate data files (extension: CLI) are necessary. For FOCUS-tier 1 -simulations only the substance data file has to be created by the user himself; the scenario and climate data files are already defined and should not be modified.

Before the user starts a PELMO simulation the scenario (location and crop, possibly irrigation) and the substance data file has to be set. The required scenario and climate input data files (*.cli and *.sze) are automatically selected by the shell and written into a small ASCII file called PELMO.INP. This file will be read by the simulation program PELMO.EXE (see Figure C.1).

The file HAUDE.DAT contains the monthly Haude-factors. This information is not used for FOCUS-simulations. However, the file must be in the FOCUS-directory of PELMO.

Figure C.1  File handling between the simulation program PELMO.EXE and the shell WPELMO.EXE

During the simulation PELMO.EXE creates a number of output files:

- ECHO.PLM:	echo of  all input parameters of the specific simulation

- WASSER.PLM:	hydrologic output data (tables)

- CHEM.PLM:	substance output data (tables)

- CHEM_xx:		metabolite output data (tables), xx=A1, A2, B1, B2, ...

- PLOT.PLM:	time series output file, used by WPELMO.EXE to create diagrams

After a PELMO simulation has been successfully performed the annual average concentrations at 1 m depth and at the soil bottom are calculated by WPELMO.EXE based on the results stored in WASSER.PLM (hydrology output), CHEM.PLM (substance output) and CHEM_xx (metabolite output). WPELMO also creates the files MBALANCE.PLM and PBALANCE.PLM that contain the total annual mass balances for water (MPBALANCE:PLM) and for the substance/metabolites (PBALANCE.PLM).

WPELMO.EXE allows archiving of simulations. If the user would like to store the results of PELMO simulations the output data files will be moved into the directory ARCHIVE using an individual extension (number between 000 and 999 instead of PLM).

### Creating substance data files for PELMO simulations

To create substance data files for PELMO using WPELMO the user has to follow two steps. First the metabolism scheme has to be defined (see Figure C.2)

Figure C.2  Edit the metabolism scheme

In the second step the user has to enter the necessary substance input data. There are specific forms for the substance (see Figure C.3) and for metabolites.

Figure C.3  Form for editing substance input data

### Running simulations using WPELMO.EXE

Using the shell WPELMO.EXE it is easy to perform PELMO-simulations After having created a substance input data file (see Figure C.2 and Figure C.3) the user has to select  a suitable crop and one of the recommended locations (see Figure C.4). The PELMO simulation will automatically start after clicking at the RUN button. It is not possible to run two PELMO simulations at the same time. Therefore, the RUN-button will be disabled as long as the current simulation is running.

Figure C.4  Running PELMO simulations using WPELMO.EXE

### Evaluating PELMO simulations using WPELMO.EXE

Using WPELMO it is easy to analyse all important results of a PELMO simulation. Specific modules of the shell generate annual average concentrations of substance and metabolites and calculate the 80th percentile. Additionally, time series diagrams of in total 23 parameters can be created with this shell. All variables can be visualised either in a cumulative or non-cumulative picture. The results of all evaluations can be transferred into other applications using the windows clipboard.

Figure C.5  Evaluating PELMO simulations using WPELMO.EXE

## Parameterisation descriptions

The implemented scenario and parameter definitions are based on:

- FOCUS DEFINITION  =  Definitions made by the FOCUS working group

- FOCUS SCENARIO SPECIFIC  =  Definitions made by the FOCUS working group for a specific scenario

- DEVELOPMENT DEFINITION  =  Definitions made during the PELMO file development

- USER INPUT  =  Input to be specified by the user in the PELMO shell

### Meteorological files (*.CLI)

| Parameter and description | Value, source & comments |
| --- | --- |
| Record 1 TITLE: label for meteorological file | FOCUS SCENARIO SPECIFIC |
| Record 2 – repeat for each day of a yr MMDDYY: meteorological month/day/year PRECIP: precipitation (cm day-1) PEVP: pan evaporation data (cm day-1) TEMP: 14h temperature per day (°C) AVTEMP: mean temperature per day (°C) VATEMP: difference between min. and max. temperature per day (°C) RELMOI: rel. humidity (%) – not used | FOCUS SCENARIO SPECIFIC Used are 9 location specific weather scenarios and 24 crop and location specific irrigated weather scenarios. |

### Soil scenario files (*.SZE)

| Parameter and description | Value, source & comments |
| --- | --- |
| Record 1 TITLE: label for scenario title | FOCUS SCENARIO SPECIFIC |
| Record 2 PFAC: pan factor used to estimate the daily potential evapotranspiration (ET) from the daily pan evaporation. SFAC: snowmelt factor in cm/degrees Celsius above freezing. IPEIND: pan factor flag ANETD: minimum depth of which evaporation is extracted (cm). INICRP: flag set to use an initial crop before first emergence. ISCOND: surface condition of initial crop | FOCUS DEFINITION - crop specific values are defined by the kc_year factors (see table with CN in record 9). These calibration factors reflect the soil surface and aerodynamic resistance as effective annual averages. set to 0.46 - DEVELOPMENT DEFINITION - SFAC is an empirical factor with wide variation. The value 0.46 represents an appropriate average based on data in the PRZM 3.12 manual and on Anderson, E.A.; 0.46 is also default value in PELMO 3.0 set to 0 = daily pan evaporation is read from the meteorological file - FOCUS DEFINITION DEVELOPMENT DEFINITION - This location specific factor is highly correlated to the climatic conditions; based on the US distribution map and the relevant 20 year average annual air temperature following values are suggested for the specific FOCUS scenarios: Scenario Avg Temp ANETD Châteaudun C 11.3 ºC 20 cm Hamburg H 9.0 °C 15 cm Jokioinen J 4.1 °C 10 cm Kremsmünster K 8.6 °C 15 cm OKEHAMPTON N 10.2 °C 15 cm PIACENZA P 13.2 °C 25 cm PORTO O 14.8 °C 25 cm SEVILLA S 17.9 °C 30 cm THIVA T 16.2 °C 30 cm Comment: This value represents soil evaporation moisture loss during a fallow, dormant period. By default evaporation is assumed to occur in the top 10 cm of soil with remaining moisture losses occurring below 10 cm up to the maximum rooting depth. Values for ANETD apply only when there is no growing season, allowing a reduced level of moisture loss through evaporation limited to the minimum depth. set to 1 = simulate initial crop - DEVELOPMENT DEFINITION set to 1 = fallow DEVELOPMENT DEFINITION |

| Record 3 ERFLAG: flag to select simulation of erosion. | set to 0 = no erosion - FOCUS DEFINITION |
| --- | --- |
| Record 4 NDC: number of different crops in the simulation. | set to 1 = only one crop - FOCUS DEFINITION |
| Record 5 – repeat up to NDC ICNCN: crop number of the different crop. CINTCP: maximum interception storage of the crop (cm). AMXDR: maximum rooting depth of the crop (cm). COVMAX: maximum areal coverage of the canopy (percent). ICNAH: surface condition of the crop after harvest date (fallow, cropping, residue). CN: runoff curve numbers of antecedent moisture condition II for fallow, cropping, residue (3 values). | set to 1 = the crop used - FOCUS DEFINITION set to zero = no rainfall interception - FOCUS DEFINITION FOCUS SCENARIO SPECIFIC FOCUS SCENARIO SPECIFIC - is set to the maximum interception percentages (crop and location specific values vary from 45% to 90%) set to 3 = residue DEVELOPMENT DEFINITION Runoff is calculated by a modification of the USDA Soil Conservation Service curve number approach (Haith et al., 1979). The curve numbers were selected based on two definitions: 1) SCS hydraulic Soil Group: The SCS group was chosen for Piacenza to be A, Hamburg to be B and for all the rest locations to be C - FOCUS DEFINITION 2) Curve Numbers: Crop and soil specific CN are defined corresponding to values of PELMO 3.0, the original USDA definition and the PRZM 3.12 manual. – DEVELOPMENT DEFINITION |

|  | SCS soil group: A B C D HTMAX PFAC - fallow + residue 77 86 91 94 - 1.00 – apples (orchards) 36 60 73 79 250 0.99 – grass (+alfalfa) 30 58 71 78 40 1.00 – potatoes 62 83 89 93 100 0.94 – sugar beet 58 72 81 85 40 0.93 – winter cereals 54 70 80 85 100 0.84 - beans (field+vegetable) 67 78 85 89 150 0.89 – bush berries 36 60 73 79 130 1.00 – cabbage 58 72 81 85 30 0.97 – carrots 58 72 81 85 40 0.96 – citrus 36 60 73 79 250 0.73 – cotton 67 78 85 89 120 0.95 – linseed 54 70 80 85 150 0.84 – maize 62 83 89 93 250 0.94 – oil seed rape (sum) 54 70 80 85 140 0.93 – oil seed rape (win) 54 70 80 85 140 0.78 – onions 58 72 81 85 60 0.91 – peas (animals) 67 78 85 89 100 0.96 – soybean 67 78 85 89 170 0.92 – spring cereals 54 70 80 85 110 0.92 – strawberries 58 72 81 85 40 1.00 – sunflower 62 83 89 93 150 0.86 – tobacco 67 78 85 89 250 0.98 – tomatoes 62 74 81 86 110 0.97 – vines 45 62 73 79 170 0.89 |
| --- | --- |
| USLEC: Universal soil loss equation cover management factor for fallow, crop and residue. WFMAX: maximum dry weight of the crop at full canopy (kg m-2). | For all perennial crops (alfalfa, apples, bushberries citrus, grass, strawberries, vines) the same CN are used for fallow and residue! Only required if ERFLAG = 1 set to 1 – DEVELOPMENT DEFINITION set to 0.0 = not used - FOCUS DEFINITION (only required if non-linear foliar application). |
| Record 6 NCPDS: number of cropping periods. | set to 66 (= longest possible simulation period) - FOCUS DEFINITION |
| Record 7 - repeat up to NCPDS E_MMDDYY: crop emergence date (month/day/year). M_MMDDYY: crop maturation date. H_MMDDYY: crop harvest date. INCROP: crop number associated with NDC | FOCUS SCENARIO SPECIFIC FOCUS SCENARIO SPECIFIC FOCUS SCENARIO SPECIFIC set to 1 (only one crop) - FOCUS DEFINITION |

| Record 8 CORED: total depth of soil core (cm) DUMMY: dummy number NCOM2 total number of simulation compartments in the soil core THFLAG: field capacity and wilting point flag. HSWZT: drainage flag. | FOCUS SCENARIO SPECIFIC former plant uptake factor, not considered here any more, this parameter is now read in from the pesticide data file. FOCUS SCENARIO SPECIFIC Scenario CORED NCOM2 Châteaudun C 260 cm 52 Hamburg H 200 cm 40 Jokioinen J 150 cm 30 Kremsmünster K 200 cm 40 OKEHAMPTON N 150 cm 30 PIACENZA P 170 cm 34 PORTO O 120 cm 24 SEVILLA S 180 cm 36 THIVA T 200 cm 40 set to 0 = the FOCUS SCENARIO SPECIFIC soil water contents are used - DEVELOPMENT DEFINITION Comment: another PELMO option would be to calculate field capacity and wilting point by internal pedotransfer rules using scenario specific clay and sand contents. set to 0 = free draining - FOCUS DEFINITION |
| --- | --- |
| Record 9 NHORIZ: total number of horizons | FOCUS SCENARIO SPECIFIC |
| Record 10a –repeat 10a-10b up to NHORIZ HORIZN: horizon number in relation to NRHORIZ. THKNS: soil horizon thickness (cm). BD: soil bulk density [g cm-3] DISP: hydrodynamic dispersion (cm2 day-1) THETO: initial soil water content in the soil horizon (cm3 cm-3) | FOCUS SCENARIO SPECIFIC FOCUS SCENARIO SPECIFIC FOCUS SCENARIO SPECIFIC set to 0, dispersion is accounted for in PELMO by numerical dispersion – FOCUS DEFINITION set to 0.2 – DEVELOPMENT DEFINITION |

| Record 10b –repeat 10a-10b up to NHORIZ THEFC: field capacity (cm3 cm-3). THEWP: wilting point (cm3 cm-3). OC: organic carbon content (%) PH: pH value Biodeg: relative biodegradation factor | FOCUS SCENARIO SPECIFIC FOCUS SCENARIO SPECIFIC FOCUS SCENARIO SPECIFIC FOCUS SCENARIO SPECIFIC depth dependent correction factor applied to the substance(s) degradation rates FOCUS DEFINITION 0 – 30 cm depth 1 30 – 60 cm depth 0.5 60 – 100 cm depth 0.3 > 100 cm depth 0 |
| --- | --- |
| Record 11 ILP: Initial level of substance indicator | set to 0 = no initial substance levels input – DEVELOPMENT DEFINITION |
| Record 12 ITEM1: Hydrology output summary indicator STEP1: Time step of hydrology output LFREQ1: Frequency of soil compartment reporting ITEM2: Substance output summary indicator STEP2: Time step of substance output LFREQ2: Frequency of soil compartment reporting ITEM3: Substance concentration profile indicator STEP3: Time step of substance concentration profile output LFREQ3: Frequency of soil compartment reporting | DEVELOPMENT DEFINITION set to YEARLY – DEVELOPMENT DEFINITION set to 1 = every compartment is output –DEVELOPMENT DEFINITION DEVELOPMENT DEFINITION set to YEARLY – DEVELOPMENT DEFINITION set to 1 = every compartment is output –DEVELOPMENT DEFINITION DEVELOPMENT DEFINITION set to YEARLY – DEVELOPMENT DEFINITION set to 1 = every compartment is output –DEVELOPMENT DEFINITION |
| Record 13 NPLOTS: Number of time series to be written to plotting file | 22 - DEVELOPMENT DEFINITION |

| Record 14 – repeat up to NPLTOTS PLNAME: Identifier of time series MODE: Plotting mode IARG: Argument of variable identified in PLNAME CONST: Constant used for unit conversion | DEVELOPMENT DEFINITION Comment: The time series identified here are requirements for the graphical output and analysis within the Graphical User Interface. They cannot be changed. |
| --- | --- |
| Record 15 ROFLAG: Runoff flag DEPRO: infiltration depth before runoff starts (cm) | set to 1 = runoff calculated – FOCUS DEFINITION set to 5.0 cm – DEVELOPMENT DEFINITION |
| Record 16 GEOBREI: Latitude | FOCUS SCENARIO SPECIFIC Comment: The geographical latitude is usually required only for calculation of the evapotranspiration by the methods of Hamon or Haude, whereas the FOCUS DEFINITION is to use daily pan evaporation data. |

### Substance file (*.PSM)

| Parameter and description | Value, source & comments |
| --- | --- |
| Comment: Text and / or lines in the substance file that are given in brackets (< >) are comments for easier understanding of the file structure and mark the beginning or end of a parameter section. These lines should not be changed. The compound parameters are described here only for the parent compound. In principle, all processes except from volatilisation are taken into account also for each metabolite. Therefore, for each metabolite to be simulated, a similar set of parameters needs to be included, leaving out only the volatilisation data. |
| Comment CTITLE: label for substance | USER INPUT |
| Soil Horizons NHORIZ: total number of soil horizons | set to 0 = not used - DEVELOPMENT DEFINITION Comment: This parameter is required if depth dependent biodegradation factors are specified in the substance file instead of the scenario file. The parameter has then to be set to the scenario specific number of horizons. |
| Number of locations N_LOC: number of locations for which applications will be defined (1-10) CROP_TYPE flag whether applications dates has been defined by abolute dates or relative to a certain crop CROP_STAGE parameter that determines the target stage for relative applications | FOCUS SCENARIO SPECIFIC / USER INPUT 0: absolute application dates numbers >0 refer to the crop number Comment: This parameter is used by the FOCUSPELMO shell only. It is not considered by the simulation model PELMO 0 = relative to emergence 1 = relative to maturation 2 = relative to harvest Comment: This parameter is used by the FOCUSPELMO shell only. It is not considered by the simulation model PELMO |
| Applications - Repeat up to N_LOC NAPS: total number of substance applications occurring at different dates (1 – 200). | FOCUS SCENARIO SPECIFIC / USER INPUT |

| Applications – repeat up to NAPS APD: Day of the month of application APM: Month of application IAPYR: Year of application TAPP: Total application rate (kg ha-1) DEPI: Depth of incorporation (cm) | USER INPUT USER INPUT USER INPUT USER INPUT USER INPUT |
| --- | --- |
| Application Mode FAM: Substance application model | USER INPUT Selectable chemical application methods are: 1 = application to soil only 2 = foliar application using the linear model 3 = non-linear foliar application using exponential filtration model Note: Foliar application needs to be activated to simulate washoff from plant foliage and degradation of foliage substance. |
| Foliar Application Parameters (only if FAM = 2 or 3) PLDKRT: Decay rate on the plant foliate (days-1) FEXTRC: Foliar extraction coefficient for substance washoff per cm of precipitation FILTRA: Filtration parameter. Only required for exponential model (FAM = 3). | Not used for FOCUS scenarios Not used for FOCUS scenarios Not used for FOCUS scenarios |
| Flags VAPFLG: Henry’s constant flag KDFLAG: KD flag | USER INPUT 0 = Henry’s constant input by user 1 = Henry’s constant calculated USER INPUT 0 = KD input by user 1 = KD calculated from KOC |

| Volatilisation HENRYK: normalised Henry’s law constant of the active substance (dimensionless). SOLUB: Solubility in water (mg L-1) MOLMAS: Molar mass (g mol-1) VAPPRE: Vapour pressure (Pa) DAIR: molecular diffusion coefficient for the substance(s) in the air (cm2 sec-1) VOLGRE: depth for volatilisation (cm) | Comment: Henry’s constant H is a ratio of a chemical’s vapour pressure to its solubility. It represents the equilibrium between the vapour and solution phases. It is quite common to normalise H with R*T using T=20°C and to express H in this way as a dimensionless number (HENRYK): HENRYK = H / (R*T) = P*M / (C*R*T) P = vapour pressure (Pa) - USER INPUT M = mol weight (g mole-1) - USER INPUT C = water solubility (mg L-1) - USER INPUT R = gas constant = 8.3144 J K-1 mole-1 T = absolute temperature (K) USER INPUT USER INPUT required for calculation of Henry’s constant - USER INPUT required for calculation of Henry’s constant - USER INPUT set to 0.1 cm – FOCUS DEFINITION |
| --- | --- |
| Plant Uptake UPTKF: plant uptake factor (between 0.000 and 1.0; describes uptake as a fraction of transpiration* dissolved phase concentration) | USER INPUT set to 0.5 for systemic compounds (default) set to 0 = no plant uptake for other compounds Other values not to be used for TIER 1 modelling! |
| Degradation - repeat for metabolisation paths A1 – D1 and Bound Residues / CO2 DKRATE: degradation rate constant (day-1) TEMP0: reference temperature for the degradation rate constant (°C) Q10: Q10-factor for degradation rate increase when temperature increases by 10°C ABSFEU: absolute reference moisture content during the degradation studies (%Vol) FELFEU: relative reference moisture content during the degradation studies (% of FC (field capacity)) FEUEXP: Exponent for the moisture dependent correction of the degradation rate constant (moisture relationship according to WALKER) | USER INPUT - Can also be entered as a DT50 value USER INPUT USER INPUT default = 2.2 - FOCUS DEFINITION USER INPUT USER INPUT Comment: either absolute or relative soil moisture has to be specified, the other parameter should be set to 0 USER INPUT default = 0.7 – FOCUS DEFINITION |
| Flag DEGFLAG: flag controlling depth dependent degradation | USER INPUT 0: degradation according to degradation factors in the scenario file 1: degradation constant with depth 2: degradation according to individual factors in the pesticide data file For TIER 1 modelling the flag should be set to 0. |
| Adsorption (if KDFLAG = 1) KOC: KOC value (ml g-1) FRNEXKOC: Freundlich exponent 1/n (dimensionless) PH_KOC: pH value PKA: pKA value FRNMIN: lower limit concentration for the non-linear sorption according to Freundlich (µg L-1) ALTERN: annual increase of adsorption (%) | USER INPUT USER INPUT USER INPUT default = 7 USER INPUT default = 20, ie in practice not used USER INPUT default = 0.01 µg L-1 USER INPUT default = 0 (no increase of sorption with time) |
| Depth Dependent Sorption and degradation (only if DEGFLAG=2) – repeat for each soil horizon KD : KD value (ml g-1) FRNEXP: Freundlich exponent 1/n (dimensionless) DEG(1): depth dependent correction of degradation rate for metabolism path A1 DEG(2): depth dependent correction of degradation rate for metabolism path B1 DEG(3): depth dependent correction of degradation rate for metabolism path C1 DEG(4): depth dependent correction of degradation rate for metabolism path D1 DEG(5): depth dependent correction of degradation rate for metabolism path BR/CO2 | USER INPUT (only considered by PELMO if kdflag = 0) USER INPUT (only considered by PELMO if kdflag = 0) USER INPUT USER INPUT USER INPUT USER INPUT USER INPUT Comment: the depth dependent correction of degradation can also be specified in the scenario file. According to FOCUS DEFINITION the depth dependent correction factors are 0 – 30 cm depth 1 30 – 60 cm depth 0.5 60 – 100 cm depth 0.3 > 100 cm depth 0 |

### Control file PELMO.INP

| Parameter and description | Value, source & comments |
| --- | --- |
| Record 1 IYEAR: number of years of simulation period ISDAY: start day of simulation ISMON: start month of simulation IEDAY: end day of simulation IEMON: end month of simulation | 26, 46, or 66 years - FOCUS DEFINITION 1 – DEVELOPMENT DEFINITION 1 - DEVELOPMENT DEFINITION 31 - DEVELOPMENT DEFINITION 12 - DEVELOPMENT DEFINITION |
| Record 2 APPLIK: scenario parameter file name | USER INPUT, FOCUS DEFINITION |
| Record 3 CHEM: substance parameter file name | USER INPUT |
| Record 4 - repeat up to (number of simulation years) KLIMA: climate file name | USER INPUT, FOCUS DEFINITION |

## References

Anderson, E.A. (1978):  Initial Parameter Values for the Snow Accumulation and Ablation Model. Part IV.2.2.1, National Weather Service River Forecast System - User's Manual, NWS/NOAA, U.S. Dept. of Commerce, Silver Springs, MD., March 31, 1978.

Carsel, R.F., C.N. Smith, L.A. Mulkey, J.D. Dean, and P. Jowise (1984).  User's manual for the pesticide root zone model (PRZM): Release 1.  EPA-600/3-84-109.  U.S. EPA, Athens, GA.

Dean, J. D., P. S. Huyakorn, A. S. Donigian, K. A. Voos, R. W. Schanz, Y. J. Meeks, and R. F. Carsel.  1989a.  Risk of Unsaturated/Saturated Transport and Transformation of Chemical Concentrations (RUSTIC).  Volume 1:  Theory and Code Verification,  EPA/600/3-89/048a.  U. S. EPA Environmental Research Laboratory, Athens, GA.

Dean, J. D., P. S. Huyakorn, A. S. Donigian, K. A. Voos, R. W. Schanz, and R. F. Carsel.  1989b.  Risk of Unsaturated/Saturated Transport and Transformation of Chemical Concentrations (RUSTIC).  Volume 2:  User's Guide,  EPA/600/3-89/048b.  U. S. EPA Environmental Research Laboratory, Athens, GA.

Fent, G., B. Jene und R. Kubiak (1998). Performance of the Pesticide Leaching Model PELMO 2.01 to predict the leaching of bromide and 14C-Benazolin in a sandy soil in comparison to results of a lysimeter- and field study. Staatliche Lehr- und Forschungsanstalt für Landwirtschaft, Weinbau und Gartenbau (SLFA) Neustadt. Poster Abstract 6B-030, IUPAC Congress Book of Abstracts, London 1998

Haith, D.A., and R.C. Loehr (Eds.) (1979):  Effectiveness of Soil and Water Conservation Practices for Pollution Control.  U.S. Environmental Protection Agency, Athens, GA.  EPA-600/3-79-106.

Jene, B. (1998): PELMO 3.00 Manual extension, Staatliche Lehr- und Forschungsanstalt für Landwirtschaft, Weinbau und Gartenbau, D-67435 Neustadt/Wstr.

Klein, M. (1991): PELMO: Pesticide Leaching Model. Fraunhofer-Institut für Umweltchemie und Ökotoxikogie, D57392 Schmallenberg.

Klein, M., M. Müller,  M. Dust, G. Görlitz, B. Gottesbüren, J. Hassink, R. Kloskowski, R. Kubiak, H. Resseler, H. Schäfer, B. Stein  and H. Vereecken (1997), Validation of the pesticide leaching model PELMO using lysimeter studies performed for registration, Chemosphere 35 No 11, 2563-2587.

OECD (1997):  Approved draft proposal for an updated OECD guidance document No. 106: Adsorption/Desorption. OECD Guidelines for Testing of Chemicals, 1-44.